Technaxx®

Wild Cam TX–44

User Manual

The Declaration of Conformity for this device is under the Internet link: www.technaxx.de/ (in bottom bar “Konformitätserklärung”). Before using the device the first time, read the user manual carefully.

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks). Free Email: support@technaxx.de

Features

( Security camera for indoor and outdoor use

( Ideal for viewing wild animals and for monitoring houses

( 2.7” CMOS sensor with 2 mega pixels

( Video and photo function are selectable

( Standby time up to ~ 290 days

( Motion and infrared sensor for night shots

( 1.2 seconds triggering time

( Motion Detection Distance up to ~ 15m

( IPX4 splash water proof

( Easy handling and installation

Table of Contents

| 1. | Introduction………..…………………..……..….... | 2 |
| --- | --- | --- |
|  | System Requirements...……...……………..… | 2 |
| 2. | Getting to know your camera…………………….. | 3 |
|  | Part Names (front and rear view)..……..… | 3 |
| 3. | Basic Camera Operation............………………… | 4 |
|  | Installing Batteries and MicroSD Card............. | 5 |
|  | Power On….......…………….…………….……. | 7 |
| 3. | Operation Mode…………….………..……………. | 8 |
|  | PIR Photo........................................................ | 9 |
|  | PIR Video........................................................ | 11 |
|  | Time Lapse...................................................... | 14 |
| 5. | Setting..........……………...……….……………… | 16 |
| 6. | TEST Mode………………...……………………… | 22 |
| 7. | Surveillance Mode………………………………… | 24 |
| 8. | Playback...................................…..……………... | 26 |
|  | Download.............…………….………………. | 26 |
|  | Playback from PC......….......………………… | 27 |
|  | Playback from Mac......….......………………… | 27 |
| 9. | Appendix…………………………………………… | 28 |
|  | Specifications………………………………….. | 28 |
|  | UI Flow............................................................. | 29 |
| 10. | Warnings & Hints | 31 |

# 1.  Introduction

## System Requirements

PC System Requirement

- Intel® Core2Duo 1.8G or AMD equivalent CPU

- Hi-speed USB2.0 port

- 1 GB RAM internal memory minimum

- HD color monitor

- nVIDIA GeForce MX440 or above, AMD (ATi) Radeon 9200 or above

- DirectX 9.0 or higher

- Windows® XP (SP2 or higher) / Windows Vista™ / Windows 7™ / Windows 8™

Note: If your system is Windows XP Service Pack I, please go to www.microsoft.com. It’s free to update your system to Windows XP SP II.

Mac System Requirement

- Power PC G5 or Intel® Core Duo processor recommended

- Hi-speed USB2.0 port

- 1 GB RAM internal memory minimum

- HD color monitor

- Mac OS™ 10.5x or above

# 2.  Getting to know your camera

## Part Names

Front View

Rear View

# 3.  Basic Camera Operation

## Installing Batteries and SD Card

- Release 2 Fastener Locks of the camera.

- Than take out the Rear Cover.

- Make sure the Power Switch of the camera is OFF.

- Install the MicroSD card. Be sure to observe the correct polarity with clipped corner on the card to the right. All the pictures and videos will be saved in the memory card.

- Install 8 brand new alkaline AA cell batteries in the battery box. Make sure to observe correct polarity.

- Put the Battery Box into the Battery Room of the camera and make sure to observe correct polarity.

- Press the Battery Box to the end of the Battery Room.  Make sure the Battery Box has fixed in the Battery Room.

## Power On

- Slide the Power Switch to ON in the left side.

- It will initial the camera system. Wait until the LCD display the default mode on the preview screen.

- Slide the Power Switch to the right side to turn off the camera.

# 4.  Operation Mode

Define use which operation mode to record image.

- Power On the camera.

- Press the Menu button to enter the Main Menu.

- Use the Up / Down key and change the Menu to Operation Mode. (Operation Mode (default) / Setting / Version)

## PIR PHOTO

- In OPERATION MODE menu, press the OK Button then the mode item is blinking.

- Use Up / Down Keys to change the operation mode to PIR PHOTO then press OK Button again. (PIR PHOTO (default) / PIR VIDEO / TIME LAPSE)

- Use Up / Down Keys to change settings of PIR PHOTO.

- Press the Menu Button and go back to the OPERATION MODE menu.

- Press the Menu Button again to exit the main menu.

- PHOTO QUALITY

Set the resolution of still picture. The higher resolution can provide high quality picture. But it needs more memory space to save and reduce the picture number of the memory card.

HIGH 5.0MP (default) / MEDIUM 2.0MP /

LOW 0.5MP / BEST 8.0MP (interpolated)

- PHOTO DELAY

Define how longer of the interval time to active the PIR sensor. The PIR sensor only activate after the end of the interval time.

These settings are amount of time when the camera wait before it will take another image.  This delay time prevents multiple images of the same object or animal.

The delay time of PIR sensor will recount after the picture captured.

5S (default) / 30M / 10M / 5M / 1M / 30S / 15S / 10S

- CONT. SHOT

Set the number of continuous shoot.

SINGLE (default) / 9 PHOTOS / 8 PHOTOS / .......

2 PHOTOS

## PIR VIDEO

- In OPERATION MODE menu, press the OK Button then the mode item is blinking.

- Use Up / Down Keys to change the operation mode to PIR VIDEO then press OK Button again.

- VIDEO QUALITY

Select a resolution size of video record. The higher resolution can provide high quality video. But it needs more memory space to save and reduce the record time of the memory card.

1280 X 720 (default) / 720 X 480

- VIDEO LENGTH

Define the time length of video record for each clip.  The camera will record a video clip and start to countdown when the PIR sensor has detected a moving object.  Then stop record when count to the end of the VIDEO LENGTH setting.

10S (default) / 5S / 2M / 1M / 30S / 20S

- VIDEO DELAY

Define how longer of the interval time to active the PIR sensor. The PIR sensor only activate after the end of the interval time.

These settings are amount of time when the camera wait before it will take another video.

The delay time of PIR sensor will recount after the video record finish.

For example: The Rec Time is 15 seconds and PIR delay time is 30 seconds.

5S (default) / 30M / 10M / 5M / 1M / 30S / 15S / 10S

- REC AUDIO

Enable or disable / mute the microphone during video record.

ON (default) / OFF

## TIME LAPSE

- In OPERATION MODE menu, press the OK Button then the mode item is blinking.

- Use Up / Down Keys to change the operation mode to TIME LAPSE then press OK Button again.

- T.L. QUALITY

Set the resolution of time lapse picture. The higher resolution can provide high quality picture. But it needs more memory space to save and reduce the picture number of the memory card.

HIGH 5.0MP (default, interpolated) / MEDIUM 2.0MP / LOW 0.5MP / BEST 8.0MP (interpolated)

- T.L. DELAY

Time Lapse is an interval capture function. You can set an interval time to take picture one by one. The camera will take a picture one by one after every 15 seconds automatic until the memory full or battery power empty or terminate it by manual.

For example: Time Lapse is 15s.

5S (default) / ....... 1S / 30M / 10M / 5M / 1M / 59S / ....... 6S

Example:

4GB		750 pictures, 28 min. 720P videos

8GB		3100 pictures, 53 min. 720P videos

16GB		6500 pictures, 109 min. 720P videos

32GB		12800 pictures, x 220 min. 720P videos

5.  Setting

For change all default settings if need.

- Power On the camera.

- Press the Menu button to enter the Main Menu.

- Use the Up / Down keys and change the Menu to Setting.

- SETUP DATE

Adjust the current date. Use the Up / Down keys to adjust the number and use the Left / Right keys to shift next item M/D/Y.

- SETUP TIME

Adjust the current time. Use the Up / Down keys to adjust the number and use the Left / Right keys to shift next item HR mm:ss.

12HR 10:50PM (default) / 24HR 22:50

- TIME START

Set the working time to start the camera function.  Use the Up / Down keys to adjust the number and use the Left / Right keys to shift next item mm:ssAM.

- TIME STOP

Set the stop time to close the camera function. Use the Up / Down keys to adjust the number and use the Left / Right keys to shift next item mm:ssAM.

Note: If the start time and stop time are the same that mean the working time is 24 hours.

- TIME SHOT

Set when the camera to take picture / record video only in the daytime, night or all day. The daytime or night was determined by the light sensor of the camera.

OFF (default) / NIGHT ONLY / DAY ONLY

- CAMERA NAME

Define a name for your camera. If you have over one camera and mount them in different places, you can designate a different name for each camera. That will be easier for you to identify these pictures / video clips were taken by which camera.

Use the Up / Down keys to change the alphabet / number and use the Left / Right keys to shift next text.

TECHNAXX (default)

- INFO BAR

Print an information stamp on the picture. You can see the record date, time and some other information from the picture directly.

ON (default) / OFF

| Temperature: | Record the temperature during this picture taken. |
| --- | --- |
| Camera Name: | Define an index name for this camera. |
| Moon Phase: | Record the moon phase of the day when this picture taken. |

| The main purpose is the active of most animals have a relation with the moon phase. This information is helpful to search the animals. |
| --- |
| Capture Time: | Record the time information when this picture taken. |
| Capture Date: | Record the date information when this picture taken. |

- LANGUAGE

Select a language version for the user interface.

ENG (default)

- TEMP UNIT

Select which temperature unit to record in the information bar.

° F (default) / ° C

- ERASE ALL

Delete all files (picture / video) in the memory card.

NO (default) / YES

Note: 1. All data will be lose and can’t restore after delete.  Make sure you have backup all data in the hard disk or other storage device before format it.

2. Strong recommend to format the memory card (FAT32) before reuse your camera which can make sure every data can be saved normally.

- RESET

Restore all settings to the default setting.

NO (default) / YES

## VERSION

Check the system firmware version of the camera.

- Power On the camera.

- Press the Menu button

to enter the Main Menu.

- Use the Up / Down keys and change the Menu to Version.

- The firmware version show on the screen.

# 6.  TEST Mode

Before use the camera. Make sure the PIR sensor work normally.

Test its sensitivity and a correct detection zone for your purpose.

- Slide the Power Switch to TEST position.

- Close the rear cover.

- Lock Fastener Locks completely then fix the camerawhere you want to monitor.

- Walk back and forth in front of the camera. The Red TEST LED will illuminate when the camera sensor has detected you. Using this method you can accurately position your camera as desired.

Note: This TEST LED does not illuminate in Surveillance mode.

# 7.  Surveillance Mode

When all settings of the camera have done completely, start the camera into the Surveillance Mode.

- Slide the Power

Switch to On.

- The Operation Mode show which record mode is in use.  The File Counter show how many files have saved in the memory card.

- The camera starts to countdown 30 seconds and show it on the Delay Time Counter.

- Before the delay time countdown completely and enter the Surveillance Mode. You can press the OK button to take picture / record video manually.

- At the last 2 seconds of the countdown, the LCD turns off the backlight.

- After the delay time countdown completely, the camera enters the Surveillance Mode and turn off the LCD after 30 seconds.

- Press any key to weak up the camera.

# 8.  Playback

## Download

- Release 2 Fastener Locks

of the camera.

- Than take out the Rear Cover.

- Make sure the Power

Switch of the camera is Off.

- Take the micro SD card out and insert it to a compatible card reader.

- You may download your record files from the "X:\DCIM\100SIMOS" folder.

## Playback from PC

The video file format is AVI which can be played by Windows Media PlayerTM with PC.

- Windows 7: The videos can be viewed by the built-in Windows Media Player TM or QuickTime TM.

- Windows XP: The videos can be viewed by the Windows Media Player TM Ver. 11.

## Playback from Mac

- Mac: Recommend play the AVI file by the VLC media playerTM.

Note: For Mac version which can be downloaded:

http://www.videolan.org/vlc/download-macosx.html

# 9.  Appendix

## Specifications

| Image Sensor | 2.7” CMOS Sensor, 2 Mega Pixels |
| --- | --- |
| Display | Digital LCD Panel |
| Lens Specification | F=2.7, f=14.1mm, 2G2P 52° View Angle Lens |
| Lens Focus | Fixed |
| White Balance | Auto |
| Exposure | Auto |
| Video Resolution | HD : 1280x720 (720p) WVGA : 720x480 |
| Video Encode | Motion JPEG |
| Audio Encode | IMA-ADPCM |
| Video File Format | AVI |
| Still Picture | 0.5M (1024x576), 2M (1920x1080) 5M (3072x1728 by interpolation) 8M (3840x2160 by interpolation) |
| Picture File Format | JPG |
| Audio Input | Built-in MIC |
| Photo Flash Type | High Power IR LED x 2 |
| Motion Detection Distance | up to 15m (depend on the environment temperature) |
| Power Source | 8 x LR6 AA batteries* (* not included) |
| Storage | MicroSDHC up to 32GB |
| Weight | 324g (without batteries) |
| Dimension | (L) 13.0 x (W) 5.5 x (H) 19.0cm |
| Package contents | Wild Cam TX-44, Belt cable, Battery box (without batteries), User Manual |

UI Flow

OPERATION MODE (default)

PIR PHOTO (default)

PHOTO QUALITY

HIGH 5.0MP (default)

MEDIUM 2.0MP

LOW 0.5MP

BEST 8.0MP

PHOTO DELAY

5 S (default)

30 M

10 M

5 M

1 M

30 S

15 S

10 S

CONT. SHOT

SINGLE (default)

9 PHOTOS

8 PHOTOS

.

.

2 PHOTOS

PIR VIDEO

VIDEO QUALITY

1280 X 720 (default)

720 X 480

VIDEO LENGTH

10 S (default)

5 S

2 M

1 M

30 S

20 S

VIDEO DELAY

5 S (default)

30 M

10 M

5 M

1 M

30 S

15 S

10 S

REC AUDIO

ON (default)

OFF

TIME LAPSE

T.L. QUALITY

HIGH 5.0MP (default)

MEDIUM 2.0MP

LOW 0.5MP

BEST 8.0MP

T.L. DELAY

05 S (default)

.

.

01 S

30 M

10 M

5 M

1 M

59 S

.

.

6 S

SETTING

SETUP DATE

01/01/14

SETUP TIME

12HR 03:45AM (default)

24HR 03:45

TIME START

06:00PM

TIME STOP

18:00PM

TIME SHOT

OFF (default)

NIGHT ONLY

DAY ONLY

CAMERA NAME

TECHNAXX

INFO BAR

ON (default)

OFF

LANGUAGE

ENG (default)

TEMP UNIT

° F (default)

° C

ERASE ALL

NO (default)

YES

DELETEING...

RESET

NO (default)

YES

PROCESSING...

VERSION

HM3:A1.01.01

10. Warnings

( Do not attempt to disassemble the device, it may result in short-circuit or even damage. ( Do not drop or shake the device, it may break internal circuit boards or mechanics. ( Keep the device in dry and ventilated environment. Avoid high humidity and high temperature. Also batteries should not be exposed to excessive heat or direct sunlight. ( Keep the device away from little children.

Security and Disposal Hints for Batteries: Hold children off batteries. When a child swallowed a battery go to a doctors place or bring the child into a hospital promptly! Look for the right polarity (+) and (--) of batteries! Always change all batteries. Never use old and new batteries or batteries of different types together. Never short, open, deform or load up batteries! Risk of injury! Never throw batteries into fire! Risk of explosion!

Hints for Environment Protection:

Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or solvents or aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany