Technaxx®

Video Sport Sunglasses Full HD 1080P TX–25 User Manual

The Declaration of Conformity for this device is under the Internet link: www.technaxx.de/ (in bottom bar “Konformitätserklärung”). Before using the device the first time, read the user manual carefully.

This device has a rechargeable battery. It must be fully charged before first use.

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks). Free Email: support@technaxx.de

# Features

( Real time video recording with sound in brilliant image quality

( HD camera lens wth 142° wide-angle and 5 Megapixel CMOS sensor

( Video resolution Full HD 1920x1080P with 25fps, AVI format

( Photo resolution interpolated 15M pixel 4480 x 3360, JPEG format

( Interchangeable sun protection lenses UV400 in 3 colours

( Built-in rechargeable Lithium-Ion-Polymer battery 400mAh

( Supports MicroSD memory cards up to 32GB (Class 10 is recommended)

( User friendly one-button operation

( Easy connection with PC/Notebook, no driver needed

( Elegant, stylish, sporty design

Package Contents: Video Sport Sunglasses Full HD 1080P TX–25, USB cable, Power adaptor 5V DC 1A, Protective case with zipper and hand loop, 1 pair of dark grey/yellow/blue lenses, Cleaning cloth, User Manual

View of product

Changing of the glasses

Changing of the glasses is very easy. Hold the center of a glass with clean fingers and klick it out of the frame, first one side, then the other. Please do it carefully, because the little pins on both side of the glass could break when handle the glass too roughly. Also handle the glasses themselves with care, otherwise scatches could appear.

Charging the built-in battery

Connect the device to a USB port on your PC or plug it into AC power with the included power adapter. While charging the red LED is blinking constantly. When the red LED turns to a solid red light the battery is fully charged. Charging time of 4 hours is recommended.

Attention: Video recording or taking pictures only is possible, when a MicroSD* card is inserted into the MicroSD card slot.

[* The card is not included in delivery!]

Formating a MicroSD card – Important Hints !

Insert a MicroSD* card and turn on device. In case the micro card is not (!) compatible with the system, the red LED turns on but blinks very slowing for 20 seconds. That is a kind of warning system that you have to format the MicroSD card before using.

Attention: When formatting a MicroSD card, all information on the card will be deleted. Therefore please save them before formatting!

Press the ON/OFF button, then the red LED flashes very fast to format the card. After formatting, you can start other operations. If there is no action during a time period of 20 seconds, the device will shut down automatically.

Start to use the sunglasses

(1) Insert a MicroSD card (max. 32GB, recommended is Class 10 high speed or above).

(2) Press the button No. 1 (ON-OFF/Recording/Play) for a few seconds, until the red LED is on to start up the device.

(3) Then the red LED is on and starts blinking. The device starts automatically recording a video when the MicroSD card is Windows FAT32 formatted. Otherwise the device turns off after 3–5 seconds!

(4) To power OFF the device, press and hold down the ON/OFF button for a few seconds, until the red LED turns off.

Recording a video

(1) Press the ON/OFF button and the device turns on and starts BLINKING RED. You are now recording a Video.

(2) Press the ON/OFF button again to stop the recording. The RED LED now is SOLID RED. When the LED is SOLID RED press the button once to take a picture or you can hold button for 3 seconds and release to start recording a video again.

(3) Every 10 minutes the device saves one file automatically.

(4) If no operation in standby status in 2 minutes, the device will shut down automatically.

Taking photos

To take photos when device in standby mode, press the ON/OFF button once to take one photo. The red LED blinks one time to indicate it is capturing and saving your photo, then the red LED returns to solid red light.

Viewing files on a computer

To view your files on a computer, simply connect the device with the enclosed USB cable to a USB port of a computer.

It will connect as a removable drive, and depending on the settings on your PC, it may automatically notify that a new hardware has been detected. If so, select Open Folder to View Files.

If it is not (!) automatically detected, click Start on your desktop. Select “My Computer” if you are using Windows, or “Computer” if your are using Windows Vista or WIN7. The device should be listed as a Removable Disk under the “Devices with Removable Storage” section.

Using the device as a Webcam

To use the device as a webcam, you first have to take out the MicroSD card from the MicroSD card slot and plug the device into a computer’s USB port. Then search for the “Standard Camera“ under “My Computer” or search under your Skype “Video setting”. If the connection is correct then a webcam screen will appear on your computer. No audio recording is possible!

Setting Time and Date

Use the USB cable to connect the device in the Standby mode with the computer. Then the device appears. Click in the root directory with the right mouse button on the drive. Then click on „New“ and on „Create Text Document“. Then create a text document file „time.txt“. Then double-click on „time.txt“ and edit as follows:

for display in the picture

2014.07.30 08:51:30    (Date and Time)

Enter this information like this and save it.

no display in the picture

2012.07.26 08:51:30    (Date and Time in the past)

Enter this information like this and save it.

Setting video resolution

Use the USB cable to connect the device in the Standby mode with the computer. The drive of the computer appears. Click in the root directory with the right mouse button on the computer drive. Then click on "New" and on create a "Text document". Then create the text document file "size.txt". Then double click on "size.txt".

For a video resolution 1280x720P with 50fps enter the number “1”.

For a video resolution 1920x1080P with 25fps enter the number "0".

For a video resolution 1440x1080P with 30fps enter the number "2".

Save and exit!

The system will be default with 1440x1080P 30fps specifications.

Viewing a video

If you plan on viewing your files on your computer, we suggest using VLC Player. The most recent version can be downloaded at no cost from http://www.videolan.org

Troubleshooting

Q: The device seems to have frozen and don’t reacting when any buttons are pressed. A: This usually occurs if the device receives too many commands in too short a time. To reset the device, press the ON/OFF button for a few seconds until the device will turn OFF.

Q: The device’s red LED is blinking faster for 10 seconds and then it turns off automatically. The device goes into stand-by mode.

A: It occurs when the MicroSD card is full. Store the information to other storage media and empty your current MicroSD card.

Q:  The device’s red LED remains shining for 10 seconds and then it turns off automatically. The device goes into stand-by mode.

A: It occurs when no MicroSD card was inserted. Insert a MicroSD card (up to 32GB).

Q: The device’s red LED is blinking fast for 4 seconds and then it turns off automatically. The device goes into stand-by mode. (If no battery power is left, the device will shut down automatically.)

A: The device is in low battery status. Charge the battery by using the USB cable or the power charger.

Q: When playing back my video, I can hear audio, but cannot see any picture.

A: This most often occurs if your computer’s media player has trouble with your files. Try using VLC player, which can be downloaded for free at http://www.videolan.org

Technical Specifications

| Lens and Sensor | HD wide angle 142° and 5 megapixels CMOS sensor |
| --- | --- |
| Video resolution | Full HD 1920x1080P with 25fps, AVI format |
| Optional Video resolutions | 1440x1080P 30fps, AVI format 720P 1280x720P 50fps, AVI format Full HD 1920x1080P 25fps, AVI format |
| Photo resolution | 15M pixel 4480 x 3360, JPEG format |
| Audio | Pure audio recording is not possible, only together with video recording |
| Memory card | MicroSD* up to 32GB (Class 10 is recommended) [*not included in delivery] |
| Battery | Built-in rechargeable lithium-ion-polymer battery 400mAh |
| Battery charging time | ~ 1,5 hour (chargeable via USB connection) |
| Battery playing time | Video recording ~ 1 hour |
| Frame material | ABS + PC |
| USB | MINI 8Pin |
| Power adapter / Power consumption | 5V DC 1A / < 0,8 W |
| Operating systems | Windows 8.1, 8, 7, Vista, XP and compatible with MAC |
| Media Player Software | Windows Media Player, Real Player, Stormcodec |
| Weight / Dimensions | 56g / (L) 16,5 x (W) 7,7 (folded bows) x (H) 4,8cm |

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or other aggressive cleaner. Wipe the cleaned device accurately. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany