Technaxx®

IP–Security Camera for

indoor usage TX-23

User Manual

# This device complies with the requirements of the standards referred to the Directive R&TTE 1999/5/EC. The Declaration of Conformity you find here: www.technaxx.de/ (in bar at the bottom “Konformitätserklärung”). Before using the device the first time, read the user manual carefully.

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks). Free Email: support@technaxx.de

If you drill a hole in the wall, please make sure that power cables, electrical cords and/or pipelines are not damaged. When using the supplied mounting material, we do not take the liability for a professional installation. You are entirely responsible to ensure that the mounting material is suitable for the particular masonry, and that the installation is done properly. When working at higher altitudes, there is danger of falling! Therefore, use suitable safeguards.

Important Hint regarding the User Manuals:

All languages of the user manual (english, german, french, spanish, italian, netherlands, polish) you find on the CD-ROM enclosed.

The english and german version of the user manual you also find as printed version enclosed.

Contents

Before using the device the first time, read the user manual carefully.

# 1.		Features & Product Description

2. 		Software Installation and Commissioning; Hardware Requirements

3.		Hardware
3.1.		Package contents
3.2.		Hints !
3.3.		Attention !

4.		Getting Started

(Learn basic function to view and video in LAN and WLAN)

4.1.		Video from a camera in the local network (LAN)
4.2.		Set Wi-Fi connection

4.3.		View the camera on the Internet (WLAN)

4.4.		Register a new account and add devices

4.5.		Main Menu

5.		Video Surveillance (Control Panel)

6.		General system settings
6.1.		Camera Settings in LAN Mode
6.1.1.	Set the IP Address
6.1.2.	Set WIFI connection
6.1.3.	Set the local video plan
6.1.4.	Alarm alerts (Email)
6.1.5.	Groups
6.1.6.	Change the device alias
6.1.7.	Restore the default settings
6.2.		Camera settings in WAN Mode
6.2.1.	Groups
6.2.	2.	Change Access password
6.2.3.	Change the camera alias
6.2.4.	Relationship between My Secure, p2pCamViewer (MAC), My Secure

7. 		Settings on the Main Menu
7.1.		Full screen

7.2.		Settings
7.2.1.	System
7.2.2.	Video
7.2.3.	Local Alarm Alerts

7.3.		Device management
7.3.1.	Add device
7.3.2.	Change management password
7.3.3.	Change watch password
7.3.4.	Restart the device

7.3.5.	Permissions setting

7.4.		Search

7.5.		Change the password (User login password)

7.6.		Log

7.7.		Help

8. 		Frequently Asked Questions – FAQ

8.1.		Video delay

8.2.		LAN cable should not be too long

8.3.		Cannot visit the IP camera in LAN

8.4.		Can visit the IP camera in LAN, but cannot view it on WLAN

8.5.		Image quality is not good enough

8.6.		Forgot your password?

8.7.		Restore to default settings

8.8.		How to remote reboot equipment?

9.		Technical Specification

10.		INSTALLATION MANUAL for Android / IOS Smart Phone

1. Features & Product Description

( Brilliant 1/4” CMOS colour sensor

( Video resolution: 640 x 480 VGA with 25fps

( Supports P2P function, easy to connect through internet

( Alarm function, automatic alarm E-mails with image

( Direct Smartphone connection via QR-code APP

( QR-code scanning from the camera label produces immediate connection

( 10 IR–LEDs and IR night vision up to 10m

( M–JPEG video compress format

( Built-in microphone

( Rotatable head of the camera: 120° vertically, 355° horizontally

( Supports 802.11.b/g/n wireless protocol

Audio output

Network

WIFI

Alarm input/output

Reset

Power input

The camera ID and password are on the QR code label of rear panel.

2.	Software Installation and Commissioning

Windows Requirements: WIN 7, WIN 8, Win 8.1, Windows XP, Windows Vista

Hardware Requirements

( 1GB RAM and 2 Core CPU for 1 camera at 1 time

( 2GB RAM and i3 or updated processor for 4 cameras at 1 time

( REMARKS: No matter how many cameras you’d like to connect, this software has no requirement for GPU (Graphic Processing Unit)

Insert the software CD into the PC drive (or download the software under: http://www.technaxx.de/support/index.php?cat=29&pro=4320)

3.	Hardware

3.1. Package Contents: IP-Security Camera for indoor usage TX-23, Power Supply, Network cable, Antenna and red cap for the antenna, Bracket and screws, Installation-CD with user manuals in 12 languages, User Manual (english and german version).

3.2. Hints !

Security and Disposal Hints for Batteries: Hold children off batteries. When a child swallowed a battery go to a doctors place or bring the child into a hospital promptly! Look for the right polarity (+) and (--) of batteries! Always change all batteries. Never use old and new batteries or batteries of different types together. Never short, open, deform or load up batteries! Risk of injury! Never throw batteries into fire! Risk of explosion!

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or solvents/aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany

3.3. Attention !

This device may only be operated with the supplied adaptor. Do not use or store the adaptor outdoor and do not operate the charger with moist or wet hands. Always remove the adaptor from socket if the device is not in use. Never open the device. The individual components of the device shall not be disassembled, repaired or modified. Unplug the device before cleaning or maintenance or connecting accessories.

4.	Getting Started (learn basic function to view and video in LAN and WLAN)

4.1. Video from a camera in the local network (LAN)

Make sure the camera was plugged in adaptor and connected with router via LAN cable first. Run My Secure and click “LAN” on the right list area, then right-click the blank area, a menu pops out similar to Figure, select "Refresh" to get the camera list in the LAN. If there is a camera, double-click the camera ID to view the live video. If popped out a prompt like “request camera video failure!", check FAQ for help.

4.2. Set WIFI connection

(b) Set SSID (Wireless router name) / Password

(1) Enable “Start WiFi setting”.

(2) Click “Scan” to choose the WIFI connection “Network name [SSID]” (it is your Wireless router name).

(3) Wireless Security Type & Data Encryption will be selected automatically after the right Network Name (SSID) is selected. Please here no manual changes!

(4) Input the WIFI connection “Password” and click “OK” to save.

4.3. View the camera on the Internet (WLAN)

Click "Login" in the area of the main list on the right, input "User Name” (Cam/ID User) and "Login password" and click "Login" button. The user name and password is on the label of the camera (see the picture below).

The User name is: Cam ID/User, and the Password is: Login password

4.4. Register a new account and add devices

If you have many cameras, you also can register a new account, and add all cameras in the same account. In this case please insert the 4 digit number Access Code.

(1) Click “Register” and input user name / password /Email.

(2) Login in via the new account.

(3) Right click on the blank area, select “Add device” on the pop up window and input camera alias / Camera ID /Access password (it is on the label of the camera).

(4) Double click the camera name to view video

Attention: when the camera lighting RED, that means the camera is in use!

4.5. Main Menu

- Settings

- Play back

- Log

- Full screen

- Device Management

- Change password

- Help

(b) Video: Set the folder of video recording and take picture / alarm view time

(c) Local alarm alerts: Set local alarm record time / capture time / alarm music.

(d) Net: Usually this is for development to test. Do not change anything.

- Device management: Add device / change password /set permission

(a)

Add other camera to this account.

This account will get the management

authority.

(b)

Change the device management

Password.

(c)

Change the device access code

(watch password).

(d)

Change device name.

(e)

Restart the device remotely.

(f)

Set permission.

(4)  Playback: Playback video on computer.

(5)  Change password: Change login password.

(6)  Log: Check system log.

(7)  Help:

Software question and answer.

5. Video Surveillance (Control Panel)

CAUTION: some function is only for special camera!

(0)  Cruise (ON/OFF): Set cruise on, the camera will auto move rotate.

(1)    Optical zoom: control camera optical zoom +/-, only for the camera has optical zoom lens.

(2)    Digital Zoom: software support 4x digital zoom

(3)    Aperture switch: set camera aperture big or small

(4)  Capture: snap picture

(5)  Record: Record video on computer

(6)  Listen: listen to the camera audio on computer

(7)  Talk: talk with camera on computer

(8)  Set motion detection area: set the motion area (only for cameras which support motion area, and for this TX-23 means the whole area!)

Set alarm sensitivity and set

area (press left button and move

to set area)

(9)   Horizontal pan (ON/OFF): set camera auto rotate horizontally

(10)  Vertical tilt (ON/OFF0: set camera auto rotate vertically

(11)  Go to pre-set position: call the camera preset (1-8)

(12)  Set preset position: set camera preset.(1-8)
(13)  Set PTZ speed : set camera rotate speed (1-10, 10 is fastest)

(14)  Vertical flip

(15)  Mirror

(16)  Set up wireless:
Enable “ Start WIFI setting”, then click scan

to search wireless router signal and select

the right wireless router name, input pass-

word. After set WIFI, the camera will auto

restart in 1–2 minutes.

(17)  Alarm log:

The camera alarm log

(18)  Setting:

Set device properties

6. 		General System Settings

6.1. 	Camera Settings in LAN Mode

6.1.1. Set the IP address

    - Set WIFI connection

(refer to 4.2. WIFI connection)

6.1.3. Set the local video plan

Press with the right mouse at the camera and select “Set the local video plan”.

Set local video record plan, the software will auto record the camera schedule on the computer after the My Secure is running, as shown below:

Enable “7*24” to record all the time from Sunday to Monday

Click “Add” to select the day it and set the start and End time for video recording

Click “Apply” to save the current video equipment plan settings.

6.1.4. Alarm alerts (Email)

6.1.5. Groups

(1) Create a Group: Right click the camera ID and select “Create a group”. Enter a name for the group in the pop-up interface.

(2) Delete a Group: Right click the group name and click "Delete group" to display the pop-up box.

(3) Add the camera to the appropriate group: Select the camera ID, hold down the left mouse button to drag the camera to the group, and then release the left mouse button.

6.1.6. Change the device alias

Set a name that easy to remember for

LAN camera. Right-click the camera ID

and select “Change the device alias” to

set a new name for the camera, as shown.

6.1.7. Restore default setting

Right click the camera ID and select

“Restore the default setting”, as shown:

REMARKS: Login password, watch

password, and the parameters of the

device like camera system, language,

video parameter, will be restored to the

factory setting. All those settings

previously saved will be lost.

The manager for the device will not be

changed back to the default manager.

6.2.	Camera settings in WLAN mode

Login in the My Secure via the camera ID (or new registered account) and password.

. H.264/MPEG4 player

( (better image quality)

. Sub-Stream Player

( (Normal image quality)

. Close H.264/MPEG4

. Close Sub Stream

6.2.1. Groups

(1) Create a Group: Right click the camera ID and select “Create a group”. Enter a name for the group in the pop-up interface.

(2) Delete a Group: Right click the group name and click "Delete group" to display the pop-up box.

(3) Add the camera to the appropriate group: Select the camera ID, hold down the left button to drag the camera to the group, and then release the left mouse button.

6.2.2. Change Access password

After successfully login in, right-click on

camera ID, select “Change access code”,

as shown:

6.2.3. Change the camera alias

Set a name that easy to remember

For LAN camera. Right-click the

camera ID and select “Change the

device alias” to set a new name for

the camera, as shown.

    - Relationship between My Secure,

p2pCamViewer (MAC), My Secure

There are different kind of software can be used in the IP camera:

(1) My Secure: for Windows PC users

(2) My Secure: for Smartphone users like Android and iPhone.

Users can use different software above to see video from one IP camera.

NOTE: modifications on one IP camera through different software are simultaneous.

In order to prevent disorder among modifications on different devices, we suggest each user should register one account for surveillance management only.

(3) QR-Code:

Except for logging in with the ID number and password on the sticker, users can also login automatically by scanning the QR-Code on the sticker.

After clicking the "Scan QR Code"

on the Smartphone the scanning

of the ID number and password

starts automatically.

Once the scanning is correct and

finished, the live video will come out

automatically on the Smartphone.

7. Settings on the Main Menu

Settings

Play back

Log

Device notify (not available)

Full screen

Device Management

Change password

Help

7.1. Full Screen

Live video in software will be in Full screen after click button “Full screen”. To exit the Full screen please click the button in the screen top right hand corner or “Esc” in the keyboard.

7.2. Settings

In “Settings”, user can do the setting for System, Video, Local Alarm Alerts and Net.

7.2.1.	System

7.2.2.	Video

Default folder for capture and video recording can be set on this page.

“Alarm view time” means the duration showing the “Device alarm” message the top left corner when the motion detection alarm is activated. “Clear record”, “Clear picture file” and “Clear login record” also can be done by this page.

7.2.3.	Local Alarm	Alerts

Before setting the Local Alarm Alerts, complete the setting on motion detection area. To learn about the setting of motion detection area, refer to No. 5. “Video Surveillance“ (8) Motion detection area”.

7.3.	Device Management

Device management function is used to manage the permission for different device and different user. Before starting the device management, make sure you login with your account which you registered.

7.3.1.	Add device

If user forgets the password, click the restore button (Refer to Section 6.1.11. “Restore the default settings”) and password will change back to the original password.

7.3.2.	Change management password

7.3.3.	Change watch password

7.3.4.	Change camera alias

Set a friendly name easy to

Remember for the camera.

7.3.4.	Restart the device

Click the button to remotely restart the device.

7.3.5.	Permissions Setting

Add permission: Input the user name and search, then select the user name and set permission levels.

Change permission: Select the user name and click “Change Permission”, then select the level by “No right”, “Allow watch”, “Allow watch and record” and “Allow watch, record and operate”.

No right: Users are not allowed to watch the live video, unless they know the watch password.

Allow watch: Users are allowed to watch live video.

Allow watch and record: Users are allowed to watch, capture and record live video.

Allow watch, record and operate:

Users are allowed to watch live video,

capture and record live video, and

change system settings, to control PTZ.

Delete permission:

If the user name is deleted, user will have

the permission to watch IP camera if the

user knew the watch password

(Access code).

7.4.	Search

According to recording time of the query video recordings on the local computer, double-click the video file to playback. NOTE: Video playback support for pause, slow down, fast forward, drag the progress bar and other operations.

  - Change password

(User login password)

When login successfully, you can click

"Change Password" button on the menu

Bar, pop-up window, input the original login

password and new password.

7.6.	Log

User can check the Log History by

clicking on the “LOG” icon.

7.7.	Help

User can check the user manual by

HTML format by clicking on the “Help”

icon on top left main menu.

8.	 FAQ (Frequently Asked Questions)

8.1. Video delay: There are three factors which will cause video delay: upload speed, PC download speed, and image resolution. If the issue happens on the PC client, generally, you can click “Settings” as below to adjust the resolution to QVGA (320 x 240). If it also does not work, please check the other two factors.

8.2. LAN cable should not be too long

If network cable is too long, the signal will be weakened and cause disconnection. Any network fault on PC client or IP camera will cause video disconnection.

8.3. Cannot visit the IP camera in LAN

1. Check whether the network cable is connected ok.

2. Right mouseclick on LAN and select “Set the IP

address”. Normally the device will automatically get

an IP address. If not, you have to set manually the

same Subnet IP address for the device.

8.4. Can visit the IP camera in LAN, but cannot view it on WLAN

When camera can be viewed on LAN, but cannot be viewed via WLAN, usually because the device gets wrong IP address. Try to set DHCP for the device

8.5. Image quality is not good enough

All of the camera parameters keep default value

of factory, but not all the parameters are proper

for special occasions. The default setting is based

on factory testing environment. Users can adjust

parameters according to his environment to get a

good video. You can adjust the parameters like

resolution to get better quality images according

to your requirements.

8.6.	Forgot your password?

If you have forgotten your own login password which registered by yourself, click “Forgot Password”. Input your username and your registered email address. The server will send a password to your mail box. Then use the new password to login.

Please check your Email

8.7. Restore to default settings

(a) Press the reset button of the camera about 1 minute.

(b) Right-click camera ID on LAN, click “Restore to default setting”.

8.8. How to reboot equipment?

User can reboot equipment whatever he/she is in local network or Internet. If the user is in LAN, right-click the device and select “Device restart”. If the user is in WLAN, click “Device management” and click the “Device restart”.

9.	 Technical Specifications

| Image Sensor | 1/4" CMOS colour sensor |
| --- | --- |
| Minimum illumination | 0.5 Lux |
| Video compression / Video frame rate | M–JPEG / 25fps |
| Internet connection | Supports P2P function, easy to connect through internet |
| Motion detection / Capture | Yes / Yes |
| Video (adjustable) | Brightness, Contrast, Sharpness, Saturation |
| Feature | Built-in microphone |
| Audio output | One audio output |
| Digital Zoom | 4x Digital Zoom |
| Audio format | ADPCM |
|  | Audio output |
|  | Alarm input/output |
| System interface | 10Base-T / 100Base-TX internet interface |
| Video stream | 16Kbps ~ 4Mbps |
| Protocol | TCP / IP |
| Wireless network | Supports 802.11.b/g/n wireless protocol |
| Infrared lights | 10 IR–LEDs |
| IR night vision | 10 m |
| Alarm input | 1 way on/off input |
| Alarm output | 1 way relay output |
| Power supply / Power consumption | External power adaptor DC 5V, 2A / 4W |
| Working temperature | –5°C up to +55°C |
| Weight / Dimensions | 282g / (L) 11 x (W) 10 x (H) 13cm |

Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany

10. Installation Manual

for Android / IOS Smartphone

Install IP Camera ( Install Mobile Phone App Technaxx My Secure Software ( Register an account ( Add cameras under this account

IP Network Camera Installation Procedure

First plug in the power cable to the IP camera. Then connect the LAN cable with the camera and the Router (see picture below).

ATTENTION: DHCP service must be enabled in the router!

(1) Before installation, make sure your phone is using 3G or WIFI

(2) Install software: Search and Install “My Secure”

in Apple APP store and Google play store.

(3) Click the APP icon to run the mobile APP

(4) Input the camera ID and password to Login camera

The My Secure icon (see below) you can find on the LOGIN screen right hand side (see the picture of the LOGIN screen). Also support click this icon to scan QR-code to auto input ID and password. Then check the camera label and input ID and password on the APP

( My Secure icon

(5) Login account. (If no accounts yet, go to register an account first and type in User name and Password). Under this account you can add Security CAM’s (go to point 10)

(6) After successful login, click on a camera to start monitoring.

(7) Press at the “OPTIONS” symbol to add a camera

|  | 1. Add other camera 2. Play camera video 3. Config camera 4. Camera list in WAN 5. Camera list in LAN 6. Video playback 7. Alarm events |
| --- | --- |
|  | 1. Select video resolution 2. “PRESET” operation 3. Audio talk (Attention: this menu functions are only for the TX-23 camera!) 4. Snap Picture 5. Video record |

(8) Setting Camera under sub menu WAN

Set video quality parameters and SD card, by clicking the sign.

ATTENTION: The configuration of the cameras is only under “Online” status possible!

( Automatic recording starts when enough disc space on the MicroSD card exists (Attention: only for the TX-24 camera!).

( Video partition size can be defined how much MB for each stream.

( Video settings: Select between sub-stream & main-stream.

( Quality: select the quality of the video (low, normal, high, good, super

( Set for Resolution, Frame rate & Stream accordingly.

(9) Setting Camera under sub menu LAN

You can select to enable or disable motion detection & select the sensitivity (high, medium, low).

After the connection to the camera is established, you see at the bottom of the Display the following symbol:

To delete or replace a picture,

simply press and hold at each

picture and select.

Press the button  to hear over headphone or to speak through microphone. Connect your headphone to your Smartphone or press on the microphone to speak. (Attention: only for the TX-23 camera!).

Press the button  to take

a picture one by one.

Press the button  to start

to start recording a video.

Press the button  to adjust or change the direction of the camera. (Attention: only for the TX-23 camera!).

You can also move the direction of the camera by pressing & holding the menu for each direction.

Press ❶ to invert the

camera horizontally.

Press ❷ to invert the

camera up or down.

Press ❸ to rotate the

camera horizontally.

Press ❹ to rotate the

camera vertically.

Press the button  to adjust

the colour of the camera.

Hold and move to the right or left

to change brightness.

Hold and move to the left or right

to change the contrast of the picture.

Hold and move to the left or right

to change the color of the picture.

(10) Register account (if successfully being registered, jump back to Step No. 3): Press “Register” first. Then fill in information, then click “OK” to complete it.

(11) Add cameras under account (if successfully being added, jump back to step No. 4): 	Login first. Then click “+”

Click “Add Device” or Scan to add a device automatically (QR Code)

Camera Alias 	= here you can give a name which you like.

Camera ID 		= find this ID under your Camera written with QR Code.

Access code 	= find this code under your Camera.

Focus the smart phone camera directly at the QR Code of the security cam.

Fill in camera information

“Device Alias” – give a name to this camera

“Device ID” – at bottom of each camera, there is a label with QR Code

“Access Pass.”

Click “Done”

to add it

At the end:

If successfully being added,

the new camera will be in the list.

# Text boxes

IP-Security Camera for indoor usage TX-23

Opening the CD and start the program "My Secure.exe"

Continue click “Next“ until the following steps were finished.

After installation finished, click below icon “My Secure” to run the software as shown.

- Right mouse click, then you see the device ID shown under LAN.

Then select “Set WIFI” on the menu popped out.

NOTE:

After saving WIFI settings the camera will restart automatically and then you can take off the LAN cable after the camera boots up successfully in 1–2 minutes and you saw the camera ID in BLUE under LAN.

Full screen: View video in full screen.

(2)

Settings: Set System, Video, Local alarm, Alerts, Net.

- System:

Set Program Lang- uage, Set 3D option, Notifications,Update

Please activate the 3D Option when you want to use Digital Zoom!

Attention: press 2x on the file you want to watch. It opens the window (see left). You press with right mouse at the display of the window and after this you can use the button displayed.

Run the My Secure, all the cameras will display in the LAN device list, double click the camera name to view the camera video. Right-click the device to set the camera parameter!

H.264/MPEG4 player (Better image quality) 
Sub-Stream Player (Normal image quality)
View all the devices in this group
Close H.264/MPEG4
Close Sub Stream
Close all videos in this group

The default setting is camera use DHCP. Camera auto gets IP address from network router.

It is a easy way for normal customer who do not know how to set IP address manually.

Activate the „Set WiFi Setting“ and press the button search. Select your “Router” Network Name and put the right password from your WiFi router. Here no more changes!

First enable the camera motion alarm function before setting the alarm alerts by Email.

Fill in the blanks of the pop-up window, click “OK”. The device will automatically take photos and sent them to the email you set. (For example: the SMTP port for Gmail is 587; Yahoo use 465).

Alarm pictures: picture No. you want to the camera to snap.

Data encryption: To set the data encryption format depend on the email box supplier.(Gmail use TLS; Yahoo use SSL)

User can do the setting for “When closing the main window”, “Exit software”, “Notification”, “3D option”, “System Upgrade” and “Set program languages” by this page.

Remind to use “3D option” and “Set program languages to” will only be activated after restart the software.

The new video file will cover the old record by setting “Loop recording” if the hard disk space is not enough for video storage, user can assign the minimum available hard disk space in the PC by setting “Keep space over”

(The default setting of software is 2 GB).

Click “Settings”, and choose “Local Alarm Alerts” setting, as shown.

Local alarm record: Tick the box and set the “Alarm record time”. Camera will start to record after the set time reached

Local alarm capture: Tick the box and choose the alarm time interval when snap.

Local alarm music: Tick the box to set the audible alarm music you like Click OK to confirm setting.

Input:

Device Alias

ID Management

Password

Watch password

Set watch permission

REMARK:

Default management password and watch password equal to the device login password and Access code on the QR code label.

IMPORTANT:

Default Manager (User) for the camera is Cam ID / User on the camera label. Manager position will be changed to other user if other user clicking in the "Device management" with the correct management password (Login/ password on product QR code label). One user can be the manager for more than one device.

Input the new management password (Equal to the login password in the QR code label), the new password will replace the login password of device on QR code label.

Input the new watch password (Equal to the Access code in QR code label) and set the watch permission, the new watch password will replace the Access code on QR code label.

This camera is private and protected, to limit the activity for registered user.

Management can assign different permission level to different user.

To set permission for different user, follow the steps below.

iPhone

iPhone

Android

Android

iPhone

iPhone

Android

Android

Android

iPhone

Android

iPhone

Android

iPhone

Android

iPhone

Android

Press the button   then you find the following picture you can select video resolution:

HD = 1300 kbps

Smooth = 800kbps

Faster = 400 kbps

When you press the button , you can take a picture directly from the camera.

Button Description

iPhone

iPhone