IP-Cam HD 1.0MP indoor

TX-60

User Manual

Security and Disposal Hints for Batteries: Hold children off batteries. When a child swallowed a battery go to a doctors place or bring the child into a hospital promptly! Look for the right polarity (+) and (–) of batteries! Always change all batteries. Never use old and new batteries or batteries of different types together. Never short, open, deform or load up batteries! Risk of injury! Never throw batteries into fire! Risk of explosion!

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or solvents/aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany

V1.0

# Table of Contents

Table of Contents	1

1   Overview	3

1.1  Key Features	4

1.2  Product Overview	5

1.3  MicroSD card	5

1.4 Hardware installation	6

2   Access the IP Camera	6

2.2 Access the Camera in LAN	6

2.3 Access the Camera in WAN	10

2.3.1 Static IP Addresses	10

2.3.2 Remote Access	11

2.4 Using the VLC player	13

2.5 IP Camera Connection to the Server	15

3   Surveillance Software GUI	16

3.1 Login Window	16

3.2  Modify the Username and Password	17

3.3  Setup Wizard	17

3.4 Surveillance Window	19

4   Advanced Camera Settings	24

4.1 Status	24

4.1.1 Device Information	24

4.1.2  Device Status	25

4.1.3  Session Status	25

4.1.4  Log	25

4.2  Basic Settings	26

4.2.1  Camera Name	26

4.2.2  Camera Time	26

4.2.3  User Accounts	27

4.2.4 Multi-Camera	29

4.2.5  Status Light	32

4.3 Network	32

4.3.1 IP Configuration	32

4.3.2 Wireless Settings	34

4.3.3  DDNS	36

4.3.4  UPnP	40

4.3.5 Port	40

4.3.6 Mail Settings	42

4.3.7  FTP Settings	43

4.3.8  P2P	44

4.4 Video	44

4.4.1  Video Settings	44

4.4.2  On Screen Display	45

4.4.4  Snapshot Settings	46

4.4.5  IR LED Schedule	47

4.5 Alarm	47

4.5.1  Motion Detection	47

4.5.2  Sound Detection	50

4.6 Record	51

4.6.1  Storage Location	51

4.6.2  Alarm Recording	51

4.6.3  Local Alarm Recording	52

4.6.4  Scheduled Recording	52

4.6.5  MICROSD Card Management	53

4.8 Firewall	54

4.9 System	54

4.9.1  Back-up & Restore	55

4.9.2  System Upgrade	55

4.9.3  Patch Installation	57

4.9.4  Factory Reset	57

4.9.5  Reboot	57

5  Playback	58

6  Appendix	59

6.1 Frequently Asked Questions	59

6.1.1  Install the add-on of Firefox browser, Google Chrome and IE Chrome.	59

6.1.2  Uninstall the add-on of Firefox browser, Google Chrome, IE Chrome	62

6.1.3  I have forgotten the administrator password	63

6.1.4  Camera can not record	63

6.1.5  Subnet does not match	64

6.1.6  No Pictures Problems	64

6.1.7  Cannot access IP camera in internet	65

6.1.8  UPnP always failed	65

6.1.9  Camera can not connect wireless	65

6.1.10  Cannot see other cameras listed	65

6.2 Default Parameters	65

6.3 Technical Specifications TX-60	66

# 1  Overview

( The indoor HD Wireless IP Camera with P2P is an integrated wireless IP Camera with a color CMOS sensor enabling viewing in High Definition resolution. It combines a high quality digital video camera, with a powerful web server, to bring clear video to your desktop and mobile devices from anywhere on your local network or over the Internet. ( Thanks to the P2P easy access technology, you do not need to do complicated Port Forwarding and DDNS settings, you just need to scan the QR code of the camera to connect it on smart phone, or input the UID on CMS software to do remote access. ( The IP Camera gives users more comprehensive control over a monitored site. The camera supports H.264 video compression technology, dramatically reducing file size and saving network bandwidth. ( The camera is based on the TCP/IP standard. There is a WEB server inside which could support Internet Explore. Therefore the management and maintenance of your device is simplified by using the network to access the website of your camera. ( The camera is designed for indoor surveillance applications such as home, retail store and office. Controlling the camera and managing images are simplified by using the provided web interface across the network utilizing wired or wireless connectivity. The IP camera provides Smart Phone APP for Android and iPhone users, then you can view your camera anywhere, anytime on your smart mobile devices.

## 1.1  Features

( 1.0MP HD Video resolution 720P with 23fps ( IR night vision ~5m & Sound Detection ( Built-in microphone & speaker ( Standard H.264 video compression (for the transmission of high definition video in narrow bandwidth network) ( Network connection RJ-45 with 10/100 Mbit/s ( Quick WLAN connection via WPS button (Wireless Protected Setup) ( Fast connection via QR-code scanning ( Cost free APP "My Technaxx IP Cam" ( Supports MicroSD cards up to 32GB ( Built-in DDNS service for worldwide access to the IP-camera ( Supported protocols: IP, TCP, UDP, HTTP, HTTPS, SMTP, FTP, DHCP, DDNS, UPnP, RTSP, ONVIF       ( Motion detection with variable detection range & automatically start of the recording ( Ideal for monitoring rooms and other indoor areas

( Video resolution: H.264 dual stream, 1.0MP 720P (1280x720, 23fps), VGA (640x480, 25fps) & (640x360), QVGA (320x240) & (320x180) ( Image Sensor: HD Color CMOS, 1.0MP, 0 Lux with 1x high power IR lamp (to switch ON/OFF via APP) ( Lens: M12 interface/f 2.8mm/F=1.8, Viewing angle horizontal 108°/diagonal 116°  ( Network: Ethernet & Wi-Fi IEEE 802.11 b/g/n, Frequency 2.412–2.484 ( Built-in WLAN antenna ( Power supply & consumption: DC 5V/1.0A & 3W maximum ( Operating temperature: –10°C up to 50°C ( Supports EZlink, Link to WiFi network easily (Wireless connection is compliant with IEEE 802.11b/g/n WiFi up to 150Mbps) ( Remotely controlled via WLAN & Internet through the standard browser Internet Explorer/Firefox/Google/Safari etc. ( Supports WEP, WPA-PSK, WPA2-PSK encryption ( Automatic alarm Email with image transfer to FTP server ( Remotely access via free APP for iOS & Android devices ("My Technaxx IP Cam" APP) ( Supports image snapshot & record schedule & IR-Cut auto switch ( Supports dual-stream & two-way audio (built-in microphone and speaker)

## 1.2  Product Overview

## 1.3  MicroSD card

This camera supports MicroSD card with a maximum size of 32GB. First plug in the MicroSD card into the MicroSD card slot (see picture on previous page) – insert it into the correct direction. When pluggin in the MicroSD card during the camera is work, the camera reboots automatically. The default storage path of alarm record files is MicroSD card. But when the available storage capacity of MicroSD card is less than 256M, old recorded files will be deleted automatically (loop recording starts).

## 1.4 Hardware installation

Rotate the base of the camera until points “a” and “b” are aligned, this allows for the mounting plate to be removed. Install the mounting plate on a wall or ceiling with supplied fixing screws, if needed. Align points “a” and “b” to insert the camera base to the mounting plate. Rotate so that points “a” and “b” are no longer aligned, this attaches the camera securely to the base.

# 2  Access the IP Camera

This chapter explains how to access the camera through browser. Go to the folder “Equipment Search Tool” and find the folder “For Windows OS”or “For Mac OS”. Copy and paste the Equipment Search Tool file to your computer, or drag it onto your Desktop.

Shortcut icon for Windows / Mac OS

## 2.2 Access the Camera in LAN

This camera supports HTTP and HTTPS protocols; you can access the camera by two ways.

(1) http:// LAN IP + HTTP Port NO.

The default HTTP port no is 88. Double click the Equipment Search Tool icon to run, and it should find the camera’s IP address automatically after you plug in the network cable.

Figure 2.1

Double click the IP address of the camera; your default browser will open to the camera login page.

(2) https:// LAN IP + HTTPS Port NO.

The default Https port no is 443. You can use the url to access the camera: https:// LAN IP + HTTPS port.

Go to Settings - Network - Port panel , you can see and change the http and https port no.

Figure 2.2

HTTPS (Hypertext Transfer Protocol over Secure Socket Layer) is a safe way to access your camera, the data transferred on the Internet will be encrypted. Since we cannot apply license for every LAN or DDNS URL, the webpage may pop up a warning like the following picture, you just need to click 'Continue to this website (not recommended). '

Open Internet Explorer if it is not already opened. Click on Tools, then click Internet Options.

Next, click the Security tab, then click the Trusted sites button.

Figure 2.3

For Firefox, you can add the trusted as the following way: Tools, Options, Advanced, View Certificates, Servers

Figure 2.4

Click View Certificates, and go to Servers option.

Figure 2.5

Go to Add Exception panel.

Figure 2.6

## 2.3 Access the Camera in WAN

### 2.3.1 Static IP Addresses

Users who have static IP addresses do not need to set DDNS service settings for remote access. When you have finished connecting the camera using the LAN IP address and port forwarding, you can access the camera directly from the Internet using the WAN IP address and port number.

How to Obtain the WAN IP address from a public website

To obtain your WAN IP address, enter the following URL in your browser: http://www.whatismyip.com.The webpage at this address will show you the current WAN IP.

Figure 2.3

Access your IP Camera from the Internet

You can access the IP Camera from the Internet (remote access). Enter the WAN IP address and port number in your standard browser. For example, you would enter http:// 183.37.28.254:85

NOTE: Make sure port forwarding is successful. You can do port forwarding two ways.

1) Login to your router to enable the “UPNP” function. You can then login to the camera as administrator, choose Network, and then choose UPnP to enable UPnP. Make sure that the status of UPnP reads “UPnP Successful” on the Device Status page.

2) Do port (HTTP port and Media port) forwarding manually.

If your router has a Virtual Server, it can do port forwarding. Add the camera’s LAN IP and port which you had set earlier to your router’s port forwarding settings.

If you plug the camera into a router, it will have a dynamic IP address and you need to set DDNS service settings to view it remotely.

### 2.3.2 Remote Access

If you want to access your camera by web browser outside of your LAN, you need to configure following configurations.

1.  Choose “Settings” on the top of the camera web page, then go to the “Network > IP Configuration” section on the left side of the screen and then uncheck the Obtain IP DHCP.

2. Enable UPnP and DDNS in the camera’s settings page. We recommend you to use the DDNS by factory default.

3. You can see the port of your camera here. If you want to set Remote Access for several cameras on the same network, you will need to change the HTTPS port for each camera.

- If the UPnP of the router has been enable, you do not need to perform following steps. Otherwise, you need to select one of the following methods to configure port forwarding on your router. For these steps, we will be using the TP-LINK brand wireless router as an example.

- If there is a UPnP function in your router：

Choose “Forwarding > UPnP”, make sure that the Current UPnP Status is Enabled.

- If there is no UPnP function in your router：

You need to manually add port forwarding, refer to the following steps. You need go to the “Forwarding > Virtual Servers” panel for setup.

- Now you can access your IP camera by https://domain name: HTTPS port via the Internet.

## 2.4 Using the VLC player

This camera supports RTSP streaming, here you can view the camera using VLC player.

RTSP URL  rtsp:// [user name][:password]@IP: port number/videosream

The part in the square brackets may be omitted.

user name & password: The user name and password to access the camera. This part can be omitted.

IP: WAN or LAN IP address.

Port number: If there is the RSTP port number on the Port page, you must only use RTSP port number. otherwise, you must only use HTTP port number.

Videostream: Here support three mode: videoMain, videoSub and audio. When the network speed is bad, here you had better select videoSub. If you select audio, you can only hear the sound but cannot see the video. For example: 	IP:  192.168.1.11

HTTP Port number:  88

User name:  admin

Password:  123

Here I can enter one of the following URLs in the VLC.

- rtsp://admin:123@192.168.1.11:88/videoMain

- rtsp:// @192.168.1.11:88/videoMain

- rtsp://:123@192.168.1.11:88/videoMain

- rtsp://admin@192.168.1.11:88/videoMain

Open the VLC and go to Media ( Open Network Stream option, then enter the URL into VLC.

Figure 2.9

Figure 2.10

Sometimes you may need to enter the user name and password again. Click OK and you can see the real-time preview.

Figure 2.11

Figure 2.12

If you cannot play the video in the VLC player, please check the port mapping. You can read Quick Installation Guide about How to configure port forwarding.

NOTE: If you modify the camera’s username or password, you had better reboot the camera, or else the

new username and password cannot take effect when you enter the authentication in the VLC.

## 2.5 IP Camera Connection to the Server

Device supports ONVIF2.2.1 protocol,You can easily access the NVR with ONVIF or server with ONVIF.

# 3 Surveillance Software GUI

Refer to the Quick Installation Guide if you install the camera at first time. After finishing quick installation, you can take time to learn the operation of the software.

## 3.1 Login Window

Figure 3.1

Check the login window above, it was divided to 5 sections from no. 1 to 4.

Section 1:  Enter the User name and password: The default administrator username is admin with a blank password, please reset the password at first using and prevent unauthorized users login the camera.

Section 2:  Stream: The camera supports two stream modes: Main stream and sub stream. If you want to access the camera form LAN, here you can select Main stream. If you want to access the camera from Internet, here we recommend sub stream.

Note: When the network bandwidth is badly you’d better select Sub Stream and the video will be more fluency.

Section 3:  Select the language: You can select the language you need via click on the language drop-down list to switch.

Section 4:  Login the camera: Click Login button and you will see the surveillance windows.(If login the camera for the first time, the page that modify the username and password will appears.)

## 3.2  Modify the Username and Password

When you log in for the first time, it will come to the operating of modify the username and password automatically.

Figure 3.2

Enter the New Username, New password and Confirm the password. Click Modify button, you will see the login page again.

## 3.3  Setup Wizard

After logging in for the first time, you will be directed to the“Setup Wizard”automatically. Here you can set the basic parameters of camera, such as camera name, camera time, wireless settings, IP configuration.

Figure 3.2

Camera Name: You could give a name for your IP camera.

Figure 3.3

System Time: Select the time zone you need to set the date, time,format, etc.

Figure 3.4

Wireless networks: Click Scan, find the SSID of your wireless router, select and enter the password.

Figure 3.5

IP: Set the IP address of the camera. You could choose to obtain an IP automatically (DHCP) or set the IP address manually according to your needs.

Figure 3.6

NOTE: It takes about 1 minute to connect the camera to your router.

## 3.4 Surveillance Window

Figure 3.7

Section1  LiveVideo / Settings/Playback buttons

:  Path to surveillance window. Click this button and back to the surveillance window

:  Path to Administrator Control Panel, Click it, and it will lead to Administrator Control Panel and do advanced settings.

: Click this button and back to the Playback panel to view the stored audio files stored in the MICROSD Card.

Section2 Multi-Device Window

The firmware inside the camera supports up to maximum of 9 cameras being monitoring at the same time. You can add other cameras in multi-device setting.

Section3 Mode/ Stream / Mirror/ Flip buttons/Zoom

Mode

1) 50HZ ---------Indoor surveillance (Region: Europe, China)

2) 60HZ ---------Indoor surveillance (Region: USA, Canada)

3) Outdoor------Outdoor surveillance

Stream

The default stream supports multiple modes, For example: HD Mode/720P/30fps/2M meanings: Stream type / Resolution / Maximum frame rate/ Bit rate. (Different models support different specific mode. )

1) Stream type: It is used to identify the stream type.

2) 720P/ VGA

The bigger the resolution, the better of the image quality is. If you are accessing the camera via internet and want to get more fluent video streaming, please select resolution VGA.

3) Maximum frame rate

When the video format is 50Hz, the maximum frame rate is 25 fps. When the video format is 60Hz, the maximum frame rate is 30 fps. You should lower frame rate when the bandwidth is limited. Normally, when the frame rate above 15, you can achieve fluently video. The maximum frame rate for each model is different, please see the “Specifications”.

4) Bit rate

Generally speaking, the larger the bit rate is, the clearer video will become. But the bit rate configuration should combine well with the network bandwidth. When the bandwidth is very narrow, and bit rate is large, that will lead to video cannot play well. You can reset the stream type on Settings -> Video -> Video Settings panel.

Figure 3.8

After changing, re-login the camera and you can see the modification.

Section 4: IR LED Lights

Click Infra led and there are three modes to adjust the infrared led: Auto, Manual and Schedule.

Auto: Select it and the camera will adjust the infra led (on or off) automatically.

Manual: Select it and you can turn on or turn off the infrared led manually.

Schedule: Select it and the IR led light will be off at the schedule period. If you want to define or change the IR led lights schedule time, please go to Settings--->Video---> IR LED Schedule page.

Section 5: Image quality settings: In this page, you can tune Hue, Brightness, Contrast, Saturation, and Sharpness to get higher quality.

Section 6: OSD (On Screen Display): If you have added time and camera name in the video, you can see it in the live window.

Go to Settings – Basic settings – Camera name panel, and you can change another device name. The default device name is anonymous.

Go to Settings – Basic settings – Camera time panel and adjust the device time.

Go to Settings – Video – On Screen Display panel, you can add or no add OSD.

Section 7: Play /Stop / Talk /Audio / Snap / Record / Full screen button

1 Play  Click it to play the video of the camera

2 Stop  Click it to stop the video of the camera

3 Talk Click the button and the icon will become to , then talk to the microphone that connected with PC, people around the camera can hear your voice. Click the icon again and stop talking.

4 Audio Click this icon, the icon will become to  you can hear the sound around the camera by the earphone or speakers that connected with PC.

5 Snapshot Click it to make snapshot and it pop-up a window which picture you snapshot, right click in the window and save the picture to anywhere you want.

6 Record Click the icon  and the camera start recording, you can see a green dot in the live window. Click again and stop recording. The default storage path is C:\IPCamRecord. You can change the storage path: Go to Settings -> Record -> Storage Location panel.

7 Full Screen Click it to make full-screen or you can double click the surveillance screen to make full-screen. Double click again and exit full-screen.

On screen Mouse Control: Right click the mouse and you can adjust the screen ration, full screen and Zoom up.

Figure 3.10

Keep ration: Select it and the camera will adjust the size of live window based on the computer monitor automatically. Sometimes there is a black border around the video, select Keep ration to get a better visual quality.

Full Screen: Select it and Click it to make full-screen, press ESC and exit full-screen.

Zoom up -> First Method:  Here is a convenient and fast solution to Zoom up/down screen by Clicking Video Screen and adjusting Mouse pulley, or by press the CTRL key and click the mouse left button.

-> Second Method: Click it and the live view will be digital zoomed up and then click Zoom Down and the live view back to original size.

Figure 3.11

When you select the Full Screen, then click right mouse, there is a Screen PTZ button.

Figure 3.12

Click the Screen PTZ button and put the mouse on the screen to indicate the camera move direction you prefer, press the left mouse, the camera will move to the corresponding direction. Loosen the mouse and stop moving. Press Esc button or double click right mouse and cancel the function.

NOTE: For Mac OS, the plug-in cannot support Onscreen Mouse Control, so you cannot allow to use it.

# 4 Advanced Camera Settings

Click the button “Settings”, goes to Administrator Control Panel to make advanced camera settings.

## 4.1 Status

Status contains four columns: Device Information, Device Status, Session Status and Log, it will show you various information about your camera.

### 4.1.1 Device Information

Camera Model: The camera model no.

Camera Name: The Device Name is a unique name that you can give to your device to help you identify it. Click Basic Settings and go to Camera name panel where you can change your camera name. The default device name is anonymous.

Camera ID: Display the wired MAC address of your camera. For example Device ID is 000C5D00008, the same MAC ID sticker is found at the bottom of the camera.

Camera Time: The system time of the device. Click Basic Settings and go to Camera time panel and adjust the time.

Application Firmware Version: Display the application firmware version of your camera.

Plug-In Version: Display the plug-in version of your camera

System Firmware Version: Display the System Firmware version of your camera.

### 4.1.2  Device Status

On this page you can see device status such as Alarm status/ Record Status ,DDNS status ,WIFI status and so on.

### 4.1.3  Session Status

Session status will display who and which IP is visiting the camera now.

### 4.1.4  Log

The log record shows who and which IP address accessed or logout the camera and when.

Reboot the camera and clear the log records.

## 4.2  Basic Settings

This section allows you to configure your camera’s Name, Time, Mail, User account and Multi-Device.

### 4.2.1  Camera Name

Default alias is anonymous. You can define a name for your camera here such as apple. Click Save to save your changes. The alias name cannot contain special characters.

### 4.2.2  Camera Time

This section allows you to configure the settings of the internal system clocks for your camera.

Time Zone: Select the time zone for your region from the drop-down menu.

Sync with NTP server: Network Time Protocol will synchronize your camera with an Internet time server. Choose the one that is closest to your camera.

Sync with PC: Select this option to synchronize the date and time of the Network Camera with your computer.

Manually: The administrator can enter the date and time manually. Note select the date and time format.

Use DST: Select the use DST, then select the daylight saving time from the drop-down menu.

Click Save button and submit your settings.

### 4.2.3  User Accounts

Here you can create users and set privilege, visitor, operator or administrator. The default user account is admin, with a blank password. You can enter the users accounts of visitor, operator and administrator manually.

How to change the password of administrator?

Firstly, select the account of administrator, then select “Change password”, enter the old password and the new password, lastly click modify to take effect.

How to add account?

Select one blank column, then enter the new user name, password and privilege, last click Add to take effect. You can see the new added account on the Account list.

Delete：Select the account which you want to delete, then click Delete button to take effect.

NOTE: The default admin account cannot be deleted, but you can add other administrator users.

### 4.2.4 Multi-Camera

If you want to view multi-surveillance screens on one window, you need to login one camera, and set it as the main device, and do Multi-Device Settings, add other cameras to the first one camera. Before you do multi-cams settings, you need to assign different port such as 81, 82, 83, 84, 85, 86, 87, 88 to the cameras if there is 8 cams installed.

The firmware within the camera can support a maximum of 9 devices monitoring all at the same time. This page you can both add MJPEG and H.264 series cameras to the first camera and view multi-surveillance screen on one window.

Add cameras in LAN

In Multi-Device Settings page, you can see all devices searched in LAN. The 1st Device is the default one. You can add more cameras in the list in LAN for monitoring. The camera’s software supports up to 9 IP Cameras online simultaneously. Click The 2nd Device and click the item in the Device List in LAN, the Alias, Host and Http Port will be filled in the boxes below automatically. Enter the correct username and password then click Add. Add more cameras in the same way.

Back to Surveillance Windows, and click Four Windows option, you will see four cameras you added.

Add cameras in WAN

If you want to view all cameras via the internet(remote computer), you will need to add them using DDNS domain name. Firstly, make sure all of the cameras you added can be accessed through the internet. (Read How to configure DDNS settings)

Login to the first camera using a DDNS domain name and port.

Click Multi-Device Settings. Choose The 2nd Device. Fill in the 2nd camera’s name, DDNS domain name, port number. Enter user name and password and then choose Add. (Figure 4.19)

1	The camera model: MJ or H264.

2	The 2nd camera’s name

3	Fill in the 2nd camera’s DDNS host not LAN IP

NOTE: The MJ series have the same HTTP Port no. and Media Port no.

4	Enter the 2nd camera’s user name and password

5	Click Add button and to take effect

NOTE: Here the Host must be entered as the second camera’s DDNS domain name, not its LAN IP.

Return to video window. You will see all of the cameras accessible through the internet. When you are away from home, you can use the first camera’s DDNS domain name and port to view all the cameras via internet.

### 4.2.5  Status Light

You can enable or disable status light.

## 4.3 Network

This section will allow you to configure your camera’s IP, DDNS, Wireless Settings, UPnP and Port.

### 4.3.1 IP Configuration

If you want to set a static IP for the camera, please go to IP Configuration page. Keep the camera in the same subnet of your router or computer.

Changing settings here is the same as using the Equipment Search Tool.

It is recommended that you use the subnet mask, gateway and DNS server from your locally attached PC. If you don’t know the subnet mask, gateway and DNS server, you can check your computer’s local area connection as follows:

Control Panel ( Network Connections ( Local Area Connections (Choose Support ( Details.

If you do not know the DNS server, you can use the same settings as the Default Gateway.

### 4.3.2 Wireless Settings

Step 1: Choose “Settings” on the top of the camera interface, and go to the “Network” panel on the left side of the screen, then click “Wireless Settings.” Click the Scan button and the camera will detect all wireless networks around the area. It should also display your router in the list.

Step 2: Click the SSID (name of your router) in the list, the corresponding information related to your network, such as the name and the encryption, will be filled into the relevant fields automatically. You will only need to fill in the password of your network. Make sure that the SSID, Encryption and the password you filled in are exactly the same for your router.

Step 3: Click on the Save button after all settings have been entered and disconnect the network cable. Never shut down the power of the camera until the IP camera is able to connect to the wireless network.

The LAN IP address will disappear on the window of Equipment Search Tool when the camera is configuring a wireless connection. Wait about 1 minute, the camera should obtain a wireless connection, and the LAN IP of the camera will show again on the window of the Equipment Search Tool. The IP address may have changed after the camera receives a wireless connection; we recommend setting a static local IP address if this IP address changes by right clicking the camera in Equipment Search Tools, setting a static IP, and pushing OK (see Figure4.36).

Congratulations! You have set up the wireless connection of the camera successfully.

NOTE: If you fail to make a wireless connection, refer to your seller or contact us directly for assistance.

WPS (Wi-Fi Protected Set-up)

Step 01: Press and hold the WPS button for two seconds.

Step 02: Press the WPS button on your router within 60 seconds. The WPS button is usually on the back or side of your router. On some routers, you may need to log in to the web interface and click on an on-screen button to activate the WPS feature. If you are not sure where the WPS buttons is on your router, please refer to your router’s User Manual.

The camera will automatically create a secure wireless connection to your router. If you have plugged in the network cable, please plug it out. The Equipment Search Tool will search the camera’s LAN IP. Make sure the PC and the camera share the same subnet.

NOTE: The security mode of router cannot be WEP, or else the WPS settings may be failed.

### 4.3.3  DDNS

Each camera has embedded a unique DDNS domain name when producing, and you can directly use the domain name, you can also use the third party domain name.

IP camera domain name

Here c29260.myipcamera.org for example. Go to option of DDNS on the Settings -> Network panel, you can see the domain name.

Now you can use http:// Domain name + HTTP Port to access the camera via internet.

Take hostname c29260.myipcamera.org and HTTP Port no. 800 for example, the accessing link of the camera via internet would be http:// c29260.myipcamera.org

Restore DDNS to factory: If you have configured Third Party DDNS successfully, but you want to use Manufacturer’s DDNS again , here click this button and start Manufacturer’s DDNS Service.

Third Party Domain Name Settings

User can also use third part DDNS, such as www.no-ip.com, www. 3322.com . Here take www.no-ip.com for example: ① Step 1, Go to the website www.no-ip.com to create a free hostname

Firstly: Login on www.no-ip.com and click No-IP Free to register.

Please register an account step by step according to instructions on www.no-ip.com

After registration, please login your email which used to register. You will receive an email from website, please click the link to activate your ACCOUNT as indicated in email.

Secondly: Login the link with the registered username and password to create your domain name.

Create the domain name step by step according to instructions on www.no-ip.com

Step 2: DO DDNS Service Settings within the Camera

Set DDNS Settings within the camera by hostname, a user name and password you’ve got from www.no-ip.com

Take hostname ycxgwp.no-ip.info, user name ipcamera, password ipcamera2012 for example.

First go to option of DDNS Settings on the administrator panel.

Second select No-Ip as a server..

Third fill ipcamera as DDNS user, fill password ipcamera2012 as DDNS password, fill ycxgwp.no-ip.info as DDNS domain and server URL, Then click save to make effect. The camera will restart and to take the DDNS settings effective.

Fourth after the restart, login the camera, and go to option of Device Status on the administrator panel, and check if the DDNS status is successful.

If failed, please double check if you have input the correct hostname, user name, and password, and try to redo the settings.

NOTE: If you have set Third Party DDNS successfully ,the Domain Name will be invalid. The Third Party DDNS and the Domain Name cannot work at the same time, the last time you configured will take effect.

② Do port forwarding within the router

Example: The camera’s LAN IP address is http://192.168.8.100:2000 , Media port no. is 9200.

First login the router, goes to the menu of Port Forwarding or Port Trigger (or named Virtue

Server on some brands of router). Take Linksys brand router as an example, Login the router, and goes to Applications & Gaming->Single Port Forwarding.

Second Create a new column by LAN IP address & HTTP Port No. of the camera within the router showed as below.

③ Use domain name to access the camera via internet

After the port forwarding is finished, you can use the domain name+ http no. to access the camera via internet. Take hostname ycxgwp.no-ip.info and http no. 2000 for example, the accessing link of the camera via internet would be http:// ycxgwp.no-ip.info:2000

### 4.3.4  UPnP

The default UPnP status is closed. You can enable UPnP, then the camera’s software will be configured for port forwarding. Back to the “Device Status” panel, you can see the UPnP status:

The camera’s software will be configured for port forwarding. There may be issues with your routers security settings, and sometimes may error. We recommend you configure port forwarding manually on your router.

### 4.3.5 Port

This camera supports HTTP Port / HTTPS Port/ ONVIF Port. HTTP Port is used to access the camera remotely.  If you want to access the camera and view the video.

HTTP port : By default, the HTTP and Media port is set to 88. Also, they can be assigned with another port number between 1 and 65535. But make sure they can’t be conflict with other existing ports like 25, 21.

Another way to change the HTTP port NO.

Step 1: Open the Equipment Search Tool, select the camera you would like to change the port of, right click on the IP address, and click on ”Network Configuration”, this brings up the network configuration box as shown in Figure 4.35 and 4.36.

Step 2: Enter the username and password of the Administrator (default username is admin with a blank password), and click “OK” to apply changes.

Step 3: Wait around 10 seconds, you’ll see that the camera’s LAN IP address has changed. In our example it was changed to 2000, so we see http://192.168.1.110:2000 in Equipment Search Tool.  Also, the LAN IP address is now fixed at a static IP address of http://192.168.1.110:2000 . This IP address will not change even if the camera is powered off and back on, the camera will remain on this LAN IP address. This is very important that a static LAN IP address is set, or you may have problems later with remote access and seeing the camera remotely if the camera loses power and reconnects on a different LAN IP address. Make sure you set a static LAN IP address!

If the camera cannot be accessed, please make sure the port forwarding is succeeded.

ONVIF port: By default, the ONVIF port is set to 888. Also, they can be assigned with another port number between 1 and 65535(except 0 and 65534). But make sure they cannot be conflict with other existing ports.

HTTPS port: The default port is 443. You can use the url to access the camera: https:// IP + HTTPS port.

RTSP port: The default port is 554. Only some IP Cameras have RTSP port.

### 4.3.6 Mail Settings

If you want the camera to send emails when motion has been detected, here Mail will need to be configured.

1	SMTP Server/ Port /Transport Layer Security Enter SMTP server for sender. SMTP port is usually set as 25. Some SMTP servers have their own port, such as 587 or 465, and Transport Layer Security usually is None. If you use Gmail, Transport Layer Security must be set to TLS or STARTTLS and SMTP Port must be set to 465 or 25 or 587, which port you choose should be decided by which Transport Layer Security you select.

2	SMTP Username/ password  ID account and password of the sender email address

3	Sender E-mail  Mailbox for sender must support SMTP

4	Receiver  Mailbox for receiver need not support SMTP,you can set 4 receivers

5	Save  Click Save to take effect

6	Test  Click Test to see if Mail has been successfully configured.

If the test success, you can see the Success behind the Test, at the same time the receivers will receive a test mail.

If the test fails with one of the following errors after clicking Test, verify that the information you entered is correct and again select Test .

1) Cannot connect to the server

2) Network Error. Please try later

3) Server Error

4) Incorrect user or password

5) The sender is denied by the server. Maybe the server need to authenticate the user, please check it and try again

6) The receiver is denied by the server. Maybe because of the anti-spam privacy of the server

7) The message is denied by the server. Maybe because of the anti-spam privacy of the server

8) The server does not support the authentication mode used by the device

### 4.3.7  FTP Settings

If you want to upload record files and images to your FTP server，you can set FTP Settings.

FTP server: If your FTP server is located on the LAN.

If you have an FTP server which you can access on the internet.

Port: Default is port 21. If changed, external FTP client program must change the server connection port accordingly.

FTP Mode: Here supports two modes: PORT and PASV.

Username/password: The FTP account and password.

Click Save to take effect.

Click Test to see if FTP has been successfully configured.

### 4.3.8  P2P

Access the IP Camera by Smart Phone (Android or iOS operating system)

First of all, you need to open the P2P function of the IP Camera at “Settings -> Network -> P2P”.

## 4.4  Video

This section allows you to configure Video stream settings, On screen display and Snapshot settings.

### 4.4.1  Video Settings

There are two ways to set the stream video settings. They are main stream video settings and sub stream video settings.

Enhanced Night video Definition: The camera will automatically drop the frame to extend the recording time in the night.

Stream Type: There are four types to identify different streams you have set. If select the HD Mode, the clearer video will become, and it will take up more bandwidth; If select the Smooth Mode, the bandwidth is very narrow, and bit rate is large, that will lead to video cannot play well. The Equilibrium Model is a value between HD Mode and Smooth Mode.

Resolution: The camera supports multiple types, For example: 960P, 720P, VGA, QVGA. The higher the resolution is, the clearer video will become. But the code flux will become larger too, and it will take up more bandwidth.

Bit Rate: Generally speaking, the larger the bit rate is, the clearer video will become. But the bit rate configuration should combine well with the network bandwidth. When the bandwidth is very narrow, and bit rate is large, that will lead to video cannot play well.

Frame Rate: Note that a larger frame size takes up more bandwidth. When the video format is 50Hz, the maximum frame rate is 25 fps. When the video format is 60Hz, the maximum frame rate is 30 fps. You should lower frame rate when the bandwidth is limited. Normally, when the frame rate above 15, you can achieve fluently video. The maximum frame rate for each model is different; please see the “Specifications”.

Key Frame Interval: The time between last key frame and next key frame. The shorter the duration, the more likely you will get a better video quality, but at the cost of higher network bandwidth consumption.

Variable bit rate: Select the Bit rate type to constant or variable. If select “Yes”, the camera will change the video bit rate according to the situation, but will not more than the maximum parameter "Bit Rate"; If select No, the Bit Rate is unchanged.

### 4.4.2  On Screen Display

This page is used to add time-stamp and device name on the video.

Display Timestamp: There are two options: Yes or NO. Select Yes and you can see the system date on the video.

Display Camera Name: There are two options: Yes or NO. Select Yes and you can see the device name on the video.

### 4.4.4  Snapshot Settings

On this page you can set the snapshot pictures’ image quality and the storage path.

Manual snap Quality: Low, Middle and High. The higher the quality, the picture will be clearer.

Pictures Save To: FTP or MICROSD card. If you have done FTP and Alarm settings, when alarming, the camera will snap pictures to the FTP or MICROSD card automatically.  If you select the FTP, you can set

the file name which the picture save to.

Enable timing to capture

To enable capture interval, follow the steps below:

1 Select Enable timing to capture

2 Capture interval:The interval time between two captures.

3 Select the capture time

- Capture anytime

Click the black button up the MON, you will see all time range turn red. When something moving in the detection area at anytime, the camera will capture.

- Specify an capture schedule

Click the week day words, the corresponding column will be selected. For example, click TUE, the all column of TUE turns to red, that means during TueMicroSDay whole day, the camera will capture.

- Press the left mouse and drag it on the time boxes, you can select the serial area,

4 Click Save button to take effect.

### 4.4.5  IR LED Schedule

On this page you can set the schedule time for switching IR LED lights. When parameter Mode is set to the Schedule on the Live Video window, at these schedule time, the IR LED lights will be turned off.

## 4.5  Alarm

### 4.5.1  Motion Detection

IP Camera supports Motion Detection Alarm, when the motion has been detected, the IP Camera will make a alarm.

To enable action detection, follow the steps below:

Step 01: Enable action detection

Step 03: Trigger interval--- The interval time between two motion detection.

Step 04: Select the alarm indicator

There are some alarm indicators:

A Camera Sound and PC Sound

if you select Camera Sound or PC Sound, when the motion has been detected, the people around the camera will hear beep alarm sound.

B Send E-mail

If you want to receive alarm emails when motion is detected, you must select Send E-mail and set Mail Settings first.

C Take Snapshot

If you select this checkbox, when the motion has been detected, the camera will snap the live view window as a still picture and load it to the FTP. Make sure you have set FTP and set FTP as the storage path in Video->Snapshot settings panel.

Capture interval: The interval time between two pictures.

D Recording

If you select this checkbox, when the motion has been detected, the camera will record automatically and store the record files to the MICROSD Card.  Make sure the camera has inserted MICROSD card and you have set the MICROSD card as the Alarm record files storage path, please go to Record -> Storage location page to verify this settings.

The default alarm record time is 30s and pre-alarm record time is 5s, please go to Record -> Alarm Record page and change the alarm time settings.

Step 05: Set detect area

Click set detect area and it pop up a window, then you can draw the detection area. Click OK button after settings. When something moving in the detection area, the camera will alarm. (The red areas indicate motion detection alarm!)

Step 06: Alarm Schedule

① Alarm anytime when motion is detected

Click the black button up the MON, you will see all time range turn red. When something moving in the detection area at anytime, the camera will alarm.

② Specify an alarm schedule

Click the week day words, the corresponding column will be selected. For example, click TUE, the all column of TUE turns to red, that means during TUESDAY whole day, when something moving in the detection area, the camera will alarm.

③ Press the left mouse and drag it on the time boxes, you can select the serial area.

Step 07: Click Save button to take effect.

When the motion has been detected during the detection time in the detection area, the camera will alarm and adopt the corresponding alarm indicators.

NOTE: You must set the detection area and detection schedule, or else there is no alarm anywhere and anytime.

### 4.5.2  Sound Detection

Only the FC2501PA, FC2501P, FC1405P and FC1405PC support this feature.

When the ambient sound over a certain decibel ,the sound alarm will be triggered.

If the Sensitivity is set to “High”, the camera will detect the sound whose more than 55db.

If the Sensitivity is set to “Medium”, the camera will detect the sound whose more than 65db.

If the Sensitivity is set to “Low”, the camera will detect the sound whose more than 75db.

If the Sensitivity is set to “Lower”, the camera will detect the sound whose more than 85db.

If the Sensitivity is set to “Lowest”, the camera will detect the sound whose more than 95db.

About the other operation of the sound detection, please refer to the ”Motion detection”.

## 4.6  Record

This section will allow you to change the record files storage path and the record time.

### 4.6.1  Storage Location

On this page you can change the alarm and manually recording storage path.

Recording Location: MICROSD card or FTP. When the camera alarmed, it will store the alarm files to the MICROSD card or FTP. Make sure the camera has been inserted the MICROSD card. On this page, you can see the available space of the MICROSD card.

Local Recording Location: For Windows OS, the location recording path is c:/ IPCamRecord, you can change another one. For MAC OS, the manual recording path is: / IPCamRecord.

Enter the local folder: Click here, You can enter the local storage folder.

### 4.6.2  Alarm Recording

On this page you can change the Pre-record time and Alarm record time.

The default Pre-recorded time is 5s and the alarm record time is 30s, you can change another time, click Save button to take effect.

### 4.6.3  Local Alarm Recording

This page you can enable the local alarm record and Local Alarm record time.

### 4.6.4  Scheduled Recording

On the page you can configure the schedule record. When the parameter Recording Location is set MICROSD Card on the Storage Location page, you can configure parameters as shown in follow figure.

When the parameter Recording Location is set FTP on the Storage Location page, you can configure parameters as shown in follow figure.

Click Save button to take effect.

### 4.6.5  MICROSD Card Management

This camera supports MICROSD Card and the max size of MICROSD card must be under 32G.

Go to the Settings (Device Status(Device Status page, you can see the MICROSD card status.

The default storage path of alarm record files is MicroSD card. When the available storage capacity of the MicroSD card is less than 256M, the old recorded files will be deleted automatically (loop recording).

## 4.8  Firewall

This section explains how to control the access permission by checking the client PC’s IP addresses. It is composed of the following columns: Block access from these IP addresses and Only allow access from these IP addresses.

Enable firewall, If you select Only allow access from these IP addresses and fill in 8 IP addresses at most, only those clients whose IP addresses listed in the Only allow access from these IP addresses can access the Network Camera. If you select Block access from these IP addresses, only those clients whose IP addresses are in the IP list cannot access the Network Camera.

Click Save to take effect.

## 4.9  System

In this panel, you can backup/restore your camera settings, upgrade the firmware to the latest version, restore the camera to default settings and reboot the device.

### 4.9.1  Back-up & Restore

Click Backup to save all the parameters you have set. These parameters will be stored in a bin file for future use. Click Browse and select the parameters file you have stored, then click Submit to restore the restore the parameters.

### 4.9.2  System Upgrade

Your current firmware version will be displayed on your screen. You may go to the Device Status( Device Information Page to check for the latest firmware versions available.

Click Browse, choose the correct bin file and then click System upgrade.

Don’t shut down the power during upgrade. After upgrading, you can see the upgrade result.

Upgrade Firmware by Equipment Search Tool

Double click the Equipment Search Tool shot icon , select the Camera IP that you want to upgrade the firmware. Then select Upgrade Firmware and enter the username and password, choose the firmware file, and upgrade.

CAUTION: If your camera works well with the current firmware, we recommend not upgrading. Please don’t upgrade the firmware unnecessarily. Your camera may be damaged if misconfigured during an upgrade.

NOTE:

- Before upgrade the firmware, please unplug the MICROSD card and reboot the camera, don’t upgrade the firmware in WAN through the web UI, or else the upgrade process may be failed.

- Please ensure you have download the correct firmware package for your camera before upgrading. Read the upgrade documentation (readme.txt file) in the upgrade package before you upgrade.

- Upon downloading the firmware check the sizes of the .bin files. They must match the size in the readme.txt file. If not, please download the firmware again until the sizes are the same. Your camera will not function correctly if a corrupt .bin file is used.

- Normally, only Device WEB UI need to be upgrade, please do not try to upgrade the Device System Firmware.

5)  Never shut down the power of the camera during upgrade until the IP camera restart and get connected.

6)  After upgrade successfully, please uninstall the old plugin and re-install it, then reset the camera to the default factory settings before using the camera.

### 4.9.3  Patch Installation

Click "Browse" to select the correct patch file, and then click "Install Patch" to install the patch. Do not turn off the power during it installing. After installing is complete, you will receive a system prompt.

### 4.9.4  Factory Reset

Click All reset and all parameters will return to factory settings if selected. This is similar to press the Reset button on the bottom of the camera.

### 4.9.5  Reboot

Click Reboot System to reboot the camera. This is similar to unplugging the power to the camera.

# 5 Playback

On this page you can view the record files stored in the MICROSD card.

Section 1 Define the Record files time and Type

: The storage path of record files

: Here supports three types: current day, current month and All records. Another way, select the time on the time&date manually.

: The type of records files, Here supports two typs: Normal record, Alarm record and All records.

: Click this button to search all record files satisfy the conditions you selected.

Continuous Play: Select the checkbox to play continuously all the record files.

Section 2  Search record files

On this panel you can see all record files satisfy the conditions you set.

Section 3  Play/Stop/Audio/Full screen buttons

Please select one record file before use these buttons.

Click this button to play the record files

Click this button to stop the record files

Open or stop audio

Click this button to make full screen, and double click left mouse to exit full screen.

# 6  Appendix

## 6.1  Frequently Asked Questions

NOTE: Any questions you would meet, please check Network connections firstly. Check the working status revealed by the indicators on the network server, hub, exchange and network card. If abnormal, check the network connections.

### 6.1.1  Install the add-on of Firefox browser, Google Chrome and IE Chrome.

Figure 6.1

Figure 6.2

Figure 6.3

Figure 6.4

Figure 6.5

Figure 6.6

### 6.1.2  Uninstall the add-on of Firefox browser, Google Chrome, IE Chrome

Figure 6.7

Figure 6.8

Figure 6.9

### 6.1.3  I have forgotten the administrator password

To reset the administrator username and password, press and hold down the RESET BUTTON for 5 seconds. Upon releasing the reset button, wait for 20 seconds, the camera will reboot and the username and password will return to the factory default administrator username and password. Please power on the camera before reset. *** Default administrator username: admin *** Default administrator password: No password

### 6.1.4  Camera can not record

Camera can not record when I click Record button or I can’t change the manually record path. When you use Windows7 or Vista, you may be not able to do manually record or change the record path because of the security settings of computer. There are two ways to resolve this problem:

- Add the camera as a trusted site to resolve this issue. The steps are: IE browser (Tool ( Internet Properties ( Security ( Trusted sites ( Sites ( Add. (2) Open IE browser, then right click, select “Run as administrator”

### 6.1.5  Subnet does not match

Check whether your ipcamera in the same subnet of your computer. The step is Control Panel ( Network Connections ( Dbclick Local Area Connections ( Choose General ( Properties.(Figure 3.23/3.24) Check subnet mask, IP address and gateways. When you set IP address please make sure they are in the same subnet. Otherwise you can't access camera.

### 6.1.6  No Pictures Problems

The video streaming is transmitted by the ActiveX controller. If ActiveX controller isn’t installed correctly you will see no video image. You can resolve this problem by this way: Download ActiveX controller and set the safety property of IE in the PC when you view it first time: IE browser ( Tool ( Internet Proper ( Security ( Custom Level ( ActiveX control and Plug-ins. Three options of front should be set to be “Enable”, The ActiveX programs read by the computer will be stored. As follows:

Enable: Download unsigned ActiveX controls

Enable: Initialize and script ActiveX controls not marked as safe

Enable: Run ActiveX controls and plug-ins

Figure 6.6

If you allow the ActiveX running, but still could not see living video. Please change another port number to try. Do not use port 88.

Figure6.7

NOTE:  Make sure that your firewall or anti-virus software does not block the camera or ActiveX. If you could not see video, please shut down firewall or anti-virus software to try again.

### 6.1.7  Cannot access IP camera in internet

- ActiveX controller is not installed correctly

- The port which camera used is blocked by Firewall or Anti-virus software. Please change another port number and try again.

- Port forwarding is not successful. Check these settings and make sure they are correct.

### 6.1.8  UPnP always failed

UPnP only contains port forwarding in our recent software. Sometimes, it may be failed to do port forwarding automatically because of firewall or anti-virus software. It also has much relation with router’s security settings. So we recommend you do port forwarding manually. You can view your camera in internet successfully after you do port forwarding manually in your router.

### 6.1.9  Camera can not connect wireless

If your camera could not connect wireless after you set wireless settings and plug out the cable. Please check whether your settings are correct or not.

Normally, camera can’t connect wireless mainly because of wrong settings.

Make sure broadcast your SSID; use the same encryption for router and camera.

### 6.1.10  Cannot see other cameras listed

Can’t see other cameras listed in multi-device when using remote access.

If you want to view all the cameras via the WAN, verify that each camera added in the multi-device settings can be accessed by using the DDNS name and port number. Use the DDNS domain name not the camera’s LAN IP. (For more details see: How to add cameras in WAN)

## 6.2  Default Parameters

Default network Parameters

IP address: obtain dynamically

Subnet mask: obtain dynamically

Gateway: obtain dynamically

DDNS: Embedded domain name

Username and password

Default username is admin with a blank password.

## 6.3  Technical specifications TX-60

| Image Sensor |
| --- |
| Sensor | High Definition Color CMOS Sensor |
| Display Resolution | 1.0M Pixels (1280 x 720 video resolution) |
| Min. illumination | 0 Lux with 1x high power IR lamp (to switch ON/OFF via APP) |
| Lens |
| Lens type / Focal length / Aperture | M12 interface / f 2.8mm / F=1.8 |
| Angle of View | Horizontal 108° & Diagonal 116° |
| Video |
| Image compression stream | H.264 dual stream |
| Image Frame Rate | 25fps (VGA), 23fps (720P) |
| Resolution | 720P (1280x720), VGA (640x480) & (640x360), QVGA (320x240) & (320x180) |
| Image adjustment | Hue, Brightness, Contrast, Saturation, Sharpness, Flip, Mirror |
| Infrared mode & night visibility | Automatic or manual IR & up to 5m |
| Network |
| Types | Ethernet & Wi-Fi IEEE 802.11 b/g/n |
| Frequency | 2.412 – 2.484 |
| EZlink | Link to WiFi network easily |
| WPS | One button push wireless connection |
| Network Protocol | IP, TCP, UDP, HTTP, HTTPS, SMTP, FTP, DHCP, DDNS, UPnP, RTSP, WPS |
| System Requirements |
| Operating system | Win XP, Win 7, Win 8.1, Win 10, Mac OS |
| Browser | Microsoft IE8 and above version or compatible browser, Mozilla Firefox, Google Chrome, Apple Safari |
| Other Features |
| Motion & Sound detection | Alarm via E-Mail, upload alarm snapshot to FTP |
| Two-way Audio | via Smartphone App or Web Client |
| WiFi and System LEDs | one system LED (Red) one WiFi LED (Green) |
| Privacy Block | set privacy area manually |
| User Accounts & Firewall | Three levels user role & supports IP Filtering |
| Memory & Reset | MicroSD card up to 32GB & Reset button |
| More Specifications |
| Power supply & consumption | DC 5V / 1.0A & 3W maximum |
| Operating temperature | –10°C ~ 50°C |
| Operating humidity | 10% ~ 80% non-condensing |
| Storage Temperature | –20°C ~ 60°C |
| Storage Humidity | 0% ~ 90% non-condensing |
| Weight / Dimensions | 103g / (L) 7.6 x (W) 7.6 x (H) 12.1cm |
| Package Contents | IP-Cam HD 1.0MP indoor, DC power adapter, USB to Micro USB charging cable, Ehernet cable, Screws, CD, User Manual |

This product includes software developed by third parties, including software which is released under the GNU General Public License Version 2 (GPL v2). This program is free software; you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation; either version 2 of the License, or (at your option) any later version. You may obtain a complete machine-readable copy of the source code for the above mentioned software under the terms of GPL v2 without charge except for the cost of media, shipping, and handling, upon written request to Technaxx GmbH & Co. KG, Kruppstraße 105, 60388 Frankfurt am Main, Germany.

This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details. You should have received a copy of the GNU General Public License along with this program; if not, write to the Free Software Foundation, Inc., 51 Franklin Street, Fifth Floor, Boston, MA  02110-1301, USA. (Notice from Technaxx: A copy of the GPL is included below).

### GNU GENERAL PUBLIC LICENSE: Version 2, June 1991 / Copyright (C) 1989, 1991 Free Software Foundation, Inc.  / 51 Franklin Street, Fifth Floor, Boston, MA  02110-1301, USA.

### Everyone is permitted to copy and distribute verbatim copies of this license document, but changing it is not allowed.

### Preamble

The licenses for most software are designed to take away your freedom to share and change it. By contrast, the GNU General Public License is intended to guarantee your freedom to share and change free software--to make sure the software is free for all its users. This General Public License applies to most of the Free Software Foundation's software and to any other program whose authors commit to using it. (Some other Free Software Foundation software is covered by the GNU Lesser General Public License instead.) You can apply it to your programs, too.

When we speak of free software, we are referring to freedom, not price. Our General Public Licenses are designed to make sure that you have the freedom to distribute copies of free software (and charge for this service if you wish), that you receive source code or can get it if you want it, that you can change the software or use pieces of it in new free programs; and that you know you can do these things.

To protect your rights, we need to make restrictions that forbid anyone to deny you these rights or to ask you to surrender the rights. These restrictions translate to certain responsibilities for you if you distribute copies of the software, or if you modify it.

For example, if you distribute copies of such a program, whether gratis or for a fee, you must give the recipients all the rights that you have. You must make sure that they, too, receive or can get the source code. And you must show them these terms so they know their rights.

We protect your rights with two steps: (1) copyright the software, and (2) offer you this license which gives you legal permission to copy, distribute and/or modify the software.

Also, for each author's protection and ours, we want to make certain that everyone understands that there is no warranty for this free software. If the software is modified by someone else and passed on, we want its recipients to know that what they have is not the original, so that any problems introduced by others will not reflect on the original authors' reputations.

Any free program is threatened constantly by software patents. We wish to avoid the danger that redistributors of a free program will individually obtain patent licenses, in effect making the program proprietary. To prevent this, we have made it clear that any patent must be licensed for everyone's free use or not licensed at all.

The precise terms and conditions for copying, distribution and modification follow.

### TERMS AND CONDITIONS FOR COPYING, DISTRIBUTION AND MODIFICATION

0. This License applies to any program or other work which contains a notice placed by the copyright holder saying it may be distributed under the terms of this General Public License. The "Program", below, refers to any such program or work, and a "work based on the Program" means either the Program or any derivative work under copyright law: that is to say, a work containing the Program or a portion of it, either verbatim or with modifications and/or translated into another language. (Hereinafter, translation is included without limitation in the term "modification".) Each licensee is addressed as "you".

Activities other than copying, distribution and modification are not covered by this License; they are outside its scope. The act of running the Program is not restricted, and the output from the Program is covered only if its contents constitute a work based on the Program (independent of having been made by running the Program). Whether that is true depends on what the Program does.

1. You may copy and distribute verbatim copies of the Program's source code as you receive it, in any medium, provided that you conspicuously and appropriately publish on each copy an appropriate copyright notice and disclaimer of warranty; keep intact all the notices that refer to this License and to the absence of any warranty; and give any other recipients of the Program a copy of this License along with the Program. You may charge a fee for the physical act of transferring a copy, and you may at your option offer warranty protection in exchange for a fee.

2. You may modify your copy or copies of the Program or any portion of it, thus forming a work based on the Program, and copy and distribute such modifications or work under the terms of Section 1 above, provided that you also meet all of these conditions:

a) You must cause the modified files to carry prominent notices stating that you changed the files and the date of any change.

b) You must cause any work that you distribute or publish, that in whole or in part contains or is derived from the Program or any part thereof, to be licensed as a whole at no charge to all third parties under the terms of this License.

c) If the modified program normally reads commands interactively when run, you must cause it, when started running for such interactive use in the most ordinary way, to print or display an announcement including an appropriate copyright notice and a notice that there is no warranty (or else, saying that you provide a warranty) and that users may redistribute the program under these conditions, and telling the user how to view a copy of this License. (Exception: if the Program itself is interactive but does not normally print such an announcement, your work based on the Program is not required to print an announcement.)

These requirements apply to the modified work as a whole. If identifiable sections of that work are not derived from the Program, and can be reasonably considered independent and separate works in themselves, then this License, and its terms, do not apply to those sections when you distribute them as separate works. But when you distribute the same sections as part of a whole which is a work based on the Program, the distribution of the whole must be on the terms of this License, whose permissions for other licensees extend to the entire whole, and thus to each and every part regardless of who wrote it.

Thus, it is not the intent of this section to claim rights or contest your rights to work written entirely by you; rather, the intent is to exercise the right to control the distribution of derivative or collective works based on the Program.

In addition, mere aggregation of another work not based on the Program with the Program (or with a work based on the Program) on a volume of a storage or distribution medium does not bring the other work under the scope of this License.

3. You may copy and distribute the Program (or a work based on it, under Section 2) in object code or executable form under the terms of Sections 1 and 2 above provided that you also do one of the following:

a) Accompany it with the complete corresponding machine-readable source code, which must be distributed under the terms of Sections 1 and 2 above on a medium customarily used for software interchange; or,

b) Accompany it with a written offer, valid for at least three years, to give any third party, for a charge no more than your cost of physically performing source distribution, a complete machine-readable copy of the corresponding source code, to be distributed under the terms of Sections 1 and 2 above on a medium customarily used for software interchange; or,

c) Accompany it with the information you received as to the offer to distribute corresponding source code. (This alternative is allowed only for noncommercial distribution and only if you received the program in object code or executable form with such an offer, in accord with Subsection b above.)

The source code for a work means the preferred form of the work for making modifications to it. For an executable work, complete source code means all the source code for all modules it contains, plus any associated interface definition files, plus the scripts used to control compilation and installation of the executable. However, as a special exception, the source code distributed need not include anything that is normally distributed (in either source or binary form) with the major components (compiler, kernel, and so on) of the operating system on which the executable runs, unless that component itself accompanies the executable.

If distribution of executable or object code is made by offering access to copy from a designated place, then offering equivalent access to copy the source code from the same place counts as distribution of the source code, even though third parties are not compelled to copy the source along with the object code.

4. You may not copy, modify, sublicense, or distribute the Program except as expressly provided under this License. Any attempt otherwise to copy, modify, sublicense or distribute the Program is void, and will automatically terminate your rights under this License. However, parties who have received copies, or rights, from you under this License will not have their licenses terminated so long as such parties remain in full compliance.

5. You are not required to accept this License, since you have not signed it. However, nothing else grants you permission to modify or distribute the Program or its derivative works. These actions are prohibited by law if you do not accept this License. Therefore, by modifying or distributing the Program (or any work based on the Program), you indicate your acceptance of this License to do so, and all its terms and conditions for copying, distributing or modifying the Program or works based on it.

6. Each time you redistribute the Program (or any work based on the Program), the recipient automatically receives a license from the original licensor to copy, distribute or modify the Program subject to these terms and conditions. You may not impose any further restrictions on the recipients' exercise of the rights granted herein. You are not responsible for enforcing compliance by third parties to this License.

7. If, as a consequence of a court judgment or allegation of patent infringement or for any other reason (not limited to patent issues), conditions are imposed on you (whether by court order, agreement or otherwise) that contradict the conditions of this License, they do not excuse you from the conditions of this License. If you cannot distribute so as to satisfy simultaneously your obligations under this License and any other pertinent obligations, then as a consequence you may not distribute the Program at all. For example, if a patent license would not permit royalty-free redistribution of the Program by all those who receive copies directly or indirectly through you, then the only way you could satisfy both it and this License would be to refrain entirely from distribution of the Program.

If any portion of this section is held invalid or unenforceable under any particular circumstance, the balance of the section is intended to apply and the section as a whole is intended to apply in other circumstances.

It is not the purpose of this section to induce you to infringe any patents or other property right claims or to contest validity of any such claims; this section has the sole purpose of protecting the integrity of the free software distribution system, which is implemented by public license practices. Many people have made generous contributions to the wide range of software distributed through that system in reliance on consistent application of that system; it is up to the author/donor to decide if he or she is willing to distribute software through any other system and a licensee cannot impose that choice.

This section is intended to make thoroughly clear what is believed to be a consequence of the rest of this License.

8. If the distribution and/or use of the Program is restricted in certain countries either by patents or by copyrighted interfaces, the original copyright holder who places the Program under this License may add an explicit geographical distribution limitation excluding those countries, so that distribution is permitted only in or among countries not thus excluded. In such case, this License incorporates the limitation as if written in the body of this License.

9. The Free Software Foundation may publish revised and/or new versions of the General Public License from time to time. Such new versions will be similar in spirit to the present version, but may differ in detail to address new problems or concerns.

Each version is given a distinguishing version number. If the Program specifies a version number of this License which applies to it and "any later version", you have the option of following the terms and conditions either of that version or of any later version published by the Free Software Foundation. If the Program does not specify a version number of this License, you may choose any version ever published by the Free Software Foundation.

10. If you wish to incorporate parts of the Program into other free programs whose distribution conditions are different, write to the author to ask for permission. For software which is copyrighted by the Free Software Foundation, write to the Free Software Foundation; we sometimes make exceptions for this. Our decision will be guided by the two goals of preserving the free status of all derivatives of our free software and of promoting the sharing and reuse of software generally.

NO WARRANTY

11. BECAUSE THE PROGRAM IS LICENSED FREE OF CHARGE, THERE IS NO WARRANTY FOR THE PROGRAM, TO THE EXTENT PERMITTED BY APPLICABLE LAW. EXCEPT WHEN OTHERWISE STATED IN WRITING THE COPYRIGHT HOLDERS AND/OR OTHER PARTIES PROVIDE THE PROGRAM "AS IS" WITHOUT WARRANTY OF ANY KIND, EITHER EXPRESSED OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE. THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF THE PROGRAM IS WITH YOU. SHOULD THE PROGRAM PROVE DEFECTIVE, YOU ASSUME THE COST OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION.

12. IN NO EVENT UNLESS REQUIRED BY APPLICABLE LAW OR AGREED TO IN WRITING WILL ANY COPYRIGHT HOLDER, OR ANY OTHER PARTY WHO MAY MODIFY AND/OR REDISTRIBUTE THE PROGRAM AS PERMITTED ABOVE, BE LIABLE TO YOU FOR DAMAGES, INCLUDING ANY GENERAL, SPECIAL, INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF THE USE OR INABILITY TO USE THE PROGRAM (INCLUDING BUT NOT LIMITED TO LOSS OF DATA OR DATA BEING RENDERED INACCURATE OR LOSSES SUSTAINED BY YOU OR THIRD PARTIES OR A FAILURE OF THE PROGRAM TO OPERATE WITH ANY OTHER PROGRAMS), EVEN IF SUCH HOLDER OR OTHER PARTY HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

### END OF TERMS AND CONDITIONS

How to Apply These Terms to Your New Programs

(1) If you develop a new program, and you want it to be of the greatest possible use to the public, the best way to achieve this is to make it free software which everyone can redistribute and change under these terms.

(2) To do so, attach the following notices to the program. It is safest to attach them to the start of each source file to most effectively convey the exclusion of warranty; and each file should have at least the "copyright" line and a pointer to where the full notice is found.

<one line to give the program's name and an idea of what it does.>

Copyright (C) <yyyy> <name of author>

(3) This program is free software; you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation; either version 2 of the License, or (at your option) any later version.

(4) This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.

(5) You should have received a copy of the GNU General Public License along with this program; if not, write to the Free Software Foundation Inc; 51 Franklin Street, Fifth Floor, Boston, MA  02110-1301, USA.

(6) Also add information on how to contact you by electronic and paper mail.

(7) If the program is interactive, make it output a short notice like this when it starts in an interactive mode:    Gnomovision version 69, Copyright (C) year name of author Gnomovision comes with ABSOLUTELY NO WARRANTY; for details type `show w'.

(8) This is free software, and you are welcome to redistribute it under certain conditions; type `show c' for details.

(9) The hypothetical commands `show w' and `show c' should show the appropriate parts of the General Public License. Of course, the commands you use may be called something other than `show w' and `show c'; they could even be mouse-clicks or menu items--whatever suits your program.

(10) You should also get your employer (if you work as a programmer) or your school, if any, to sign a "copyright disclaimer" for the program, if necessary. Here is a sample; alter the names:

(11) Yoyodyne, Inc., hereby disclaims all copyright interest in the program `Gnomovision' (which makes passes at compilers) written by James Hacker.

<signature of Ty Coon>, 1 April 1989	[Ty Coon, President of Vice]

(12) This General Public License does not permit incorporating your program into proprietary programs. If your program is a subroutine library, you may consider it more useful to permit linking proprietary applications with the library. If this is what you want to do, use the GNU Lesser General Public License instead of this License.

# Text boxes

LAN

WPS / Reset

Power

MicroSD card slot

Enter the camera’s url , here take https://192.168.8.129:443  for example .

Click this button to add it .

IP Address: Set this in the same subnet as your computer, or keep it as default.

Subnet Mask: Keep it as default.

Gateway and DNS Server: Set it to the IP address of your router.

Select Yes and click Save.

Click Enable DDNS and click Save.

The content in the Manufacture’s DDNS column is the domain name of your camera.

Click Add New.

Input the port and IP address of your camera and click Save.

Here you have finished the Port Forwarding setup.

7

6

5

4

3

2

1

Fill in one page number, click Go button and go to the corresponding page.

Click the page number and go to the corresponding page to see more logs.

2 Enter the User name and password of the 2nd camera

3 Click Add to take effect

1 Click it, camera model, alias, host and HTTP Port will be filled in the following boxes automatically

Use DDNS domain name

and port to login.

Make sure each camera you need add could login with DDNS name and port.

Click here

There are two DNS servers, you can set any of them. Same with gateway is also OK.

Set the same Subnet Mask and gateway of the camera with your PC.

Click the Scan button to search for wireless networks.

2 Enter the password of your router

1 Click the SSID of your router and the relevant information will be filled in the fields automatically.

WPS Button

Click here to register

Fill the Media Port no. of the camera on the column of External Port and Internal Port

Assign a name as you like here

Select which camera you’d like to change the port for, and right click .

Enter the Username and password, click OK.

Modify the Http Port .

Click this button and select all time range

Power Light

Infrared Lamp Array

Lens

Induction IC

Network Light

Microphone

1

2

3