Technaxx® * User Manual

Desk Clock with FullHD Camera TX-76

The Declaration of Conformity for this device is under the Internet link: www.technaxx.de/ (in bottom bar “Konformitätserklärung”). Before using the device the first time, read the user manual carefully.

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks). Free Email: support@technaxx.de

(!) Before the first use make sure you have charged the device.

(!!) Only use battery type 14500 lithium-ion which is included in package contents. For other batteries we do not overtake any guarantee.

(!!!) Insert a MicroSD card first, otherwise the function of the described indicator lights does not fit the description.

Features

( Digital Desk Clock with integrated FullHD camera for video and photo recordings, motion detection, night vision & alarm clock function ( Home and office surveillance ( Digital time display, also while recording ( Set up to 3 alarm times ( Video recording with sound & take pictures easily using the remote control ( Video recording with sound by motion detection (up to ~5m) ( 6x IR LED for night vision mode up to ~1–3m ( Remote control up to ~10m (open space) ( Supports recording while charging ( Easy handling and small size

Technical specifications

| Video resolution | 1920 x 1080 interpolated, AVI format, 30fps |
| --- | --- |
| Photo resolution | 2560 x 1440, JPEG format |
| Sensor | CMOS sensor, 1280 x 720, 2 MP interpolated, 60° viewing angle |
| Storage medium | Supports MicroSD(HC) cards up to 32GB (up to Class 6) |
| Playback software | VLC Player / Media player |
| Power supply | Rechargeable replaceable 2x 600mAh lithium ion batteries type 14500 3.7V or with DC 5V/1A power adapter (not included) |
| Charging time / Continuous recording time | ~5 hours / ~7 hours |
| Standby time | video-photo-function ~6 days / only clock ~11 days |
| Power consumption | 160mA/3.7V (only video), 150mA/3.7V (only IR), 30mA/3.7V (only clock) |
| Operation systems | Win7 / 8 / 8.1 / 10 |
| Weight Dimensions | 136g (with batteries), 100g (without batteries) (L) 10.4 x (W) 4.4 x (H) 4.9cm |
| Package Contents | Desk Clock with FullHD camera TX-76, 2x batteries (type 14500 3.7V), Remote control (incl. button cell battery CR2032 3V), Micro USB cable (for charging & data transfer to the PC), User Manual |

Notice: This device support 1080P video. Use high speed memory card due to large video files will leave 0.7GB space.

Introduction: it is a HD (1080P 30fps) IR (infrared) device with clock, camera, remote control, external MicroSD card and functions of video recording with sound / photo taking / motion detection / alarm clock / digital clock. It is equipped with high-capacity batteries. It support up to 32GB MicroSD card, uninterruptible long-time work and remote control.

View of device * Front side

| 6 IR LED | Up |
| --- | --- |
| Set | Camera |
| Down | LCD |

View of device * Rear side

| On/Off Switch | KEY 2 |
| --- | --- |
| MicroSD card (TF slot) | Speaker |
| Micro USB port | 1 RED LED |
| Power On/Off switch | 2 BLUE LED |
| KEY 1 | 14500 battery type |

Inserting and charging the batteries

Open the back cover of the desk clock. Install the rechargeable batteries (type: 14500 600mAh 3.7V). Ensure correct polarity of the rechargeable batteries. After inserting the batteries, close the battery compartment cover by replacing the back cover. To charge the batteries, use the attached Micro USB cable. During charging process the LED is slowly flashing BLUE. The BLUE LED is steady on when fully charged.

Inserting the memory card

NOTE: Format the memory card (up to 32GB) first in FAT32 before using it for the first time. A MicroSD must be installed before operating the camera function of the desk clock. Ensure that the contacts of the memory card face the battery compartment and are inserted first. Press the memory card into the TF card slot until you hear a click tone. To remove the memory card, push it. Then it will slide partially out of the desk clock.

Function setting

| Current time setting: Press SET once to set up hour, press UP/DOWN to select current time, press SET to set up minutes, press UP/DOWN to select current minutes, then press SET again to finish setting. (See images on the right). Note: Press long UP/DOWN for fast changing of hour and minutes. | Time mode |  |
| --- | --- | --- |
|  | Hour setting |  |
|  | Minute setting |  |

| Under time mode: Press UP to turn 12/24 hour conversion. Press DOWN to check alarm time. | 12 hours system |  |
| --- | --- | --- |
|  | 24 hours system |  |
|  | Alarm ① |  |
|  | Alarm ② |  |
|  | Alarm ③ |  |

| Alarm setting: After time setting, press SET into the ( alarm mode. Set hour first. Press SET a second time to set Alarm minute by using the UP and DOWN button, then press SET again. The screen will show A.L ON or A.L OF (see images on the right). After finish ① Alarm, press SET into ( or ( alarm setting, same way as (. Note: When 20 second without any operation the device returns back to display time mode. |  | ① Alarm mode | ② Alarm mode | ③ Alarm mode |
| --- | --- | --- | --- | --- |
|  | Alarm hour setting |  |  |  |
|  | Alarm minute setting |  |  |  |
|  | Alarm On |  |  |  |
|  | Alarm Off |  |  |  |

Use of the device

Open back cover, plug MicroSD card in and turn ON switch. In Battery mode long press  (or on remote control A button), the BLUE and RED LED will light on. After the initialization the BLUE LED turns on steady. Note: If no MicroSD card is inserted the RED LED starts flashing fast and stops after a few seconds.

Button and indicator LED description

1. Photo taking: Under standby mode (BLUE LED steady), press  KEY (or remote control A button) to activate the automatic photo taking mode (BLUE LED slowly flashing), taking 1 photo every 10 second, short press  KEY (or remote control A button) to go back to the standby mode.

2. Video recording: Under standby mode, press KEY1 (or remote control B button), BLUE LED turns off, RED LED lights on. Press KEY1 (or remote control B button) again. The RED LED flashes three times then goes off. You entered into video recording mode now. Note: Maximum file length of video recording are 10 minutes, after that a new file is created.

To save the video: Short press KEY1 (or remote control B button), RED and BLUE LED light on at same time, then red light steady on while blue light is off. Press KEY1 (or remote control B button) to enter into standby mode.

3. Motion detection: Under standby mode, short press KEY2 (or remote control C button), RED and BLUE LED flash short once. To enter into motion detection mode press KEY2 (or remote control C button) again, RED and BLUE LED starts flashing constantly. When motion is detected the RED and BLUE LED turn off. To exit motion detection mode, press KEY2 to enter into standby mode. Note: Min. file length of video recording are 30 seconds. Max. file length of video recording are 10 minutes, after that a new file is created.

4. Infra-Red Mode: Under any mode after switch on, long press Key 2 or short press D button on remote control. RED LED flashes 2x ( infrared light is enabled. RED LED flashes 1x ( infrared light is closed.

5. Recording while charging: Power switch has to be on position OFF. You also have to wait about 10 seconds before operating with the device. Important: Do not press  KEY or A button long to enable! First press A short to enable and switch between the mode. While USB charger is connected, you can enable photo mode, video mode and motion detection mode to record video/take pictures while charging. It is also possible to enable/disable the IR-LED.

6. USB mode: Connect the device via the Micro USB cable with the computer to enter into USB disk mode. In USB charging mode the BLUE LED flashes. When fully charged the BLUE LED is steady on. When no MicroSD card is inserted while switching on, RED LED flashes 10 second then switch off. While working, RED LED flashes 10 second and powers off when low battery. To switch between modes just press the corresponding KEY mentioned in the table below until the described LED is flashing. Long press the power  KEY (or remote control A button), BLUE and RED LED light up at the same time for 2 second and turn off. Now the device is in standby mode.

| BLUE LED steady | Photo taking standby | Switch mode by pressing KEY or A button on remote control |
| --- | --- | --- |
| BLUE LED flashing slowly | Photo taking every 10seconds |  |
| RED LED steady | Video recording standby | Switch mode by pressing KEY 1 or B button on remote control |
| RED LED flashing 3x than turns off | Video recording (max. file length are 10 min. per file) |  |
| BLUE and RED LED steady | Motion detection standby | Switch mode by pressing KEY 2 short or C button on remote control |
| BLUE and RED LED are flashing when no motion is detected | Motion detection is ready to record video |  |
| BLUE and RED LED OFF | Video recording when motion is detected (max. file length are 10 minutes per file) |  |
| RED LED is flashing 2x | Infra-Red Mode enabled | Switch mode by pressing KEY 2 long or button D short on remote control |
| RED LED is flashing 1x | Infra-Red Mode disabled |  |

Set Date stamp and Time stamp

The date and time will be revised for video and photo in next recording. Create a “time document” first. Note: it does not (!) work by just changing the <time.txt> document on the MicroSD card. It has to be changed via the computer connection.

1. Plug in the USB cable to the camera and to the computer.

2. Go to <My Computer> or Computer or Explorer.

3. The camera will be recognized as removable Disk Drive.

4. Double left click on removable Disk Drive and it will bring up the Photo & Video folder. DO NOT OPEN THEM !

5. Edit the text document named “time” by double left click on the ”time.txt” document.

6. Fill in the current Year.Month.Day. hour:minute:seconds [eg: 2016.06.04. 07:30:29]

- Go to File and Save, then close file.

- Power off the device and restart. The device now has the current date and the current time.

Warnings

( Do not attempt to disassemble the device, it may result in short-circuit or even damage. ( Do not drop or shake the device, it may break internal circuit boards or mechanics. ( Use it under normal temperature and normal humidiy. ( Do not put it in a moist working environment since it is not waterproof. ( Do not use it directly against strong light, to avoid damage optical device. ( Do not use under high dust density environment, to avoid the lens and other components stain dust and effect the camera quality. ( Do not make its strong shock, vibration, do not use under high magnetic field. ( Keep the device away from little children.

Security and Disposal Hints for Batteries: Hold children off batteries. When a child swallowed a battery go to a doctors place or bring the child into a hospital promptly! Look for the right polarity (+) and (–) of batteries! Always change all batteries. Never use old and new batteries or batteries of different types together. Never short, open, deform or load up batteries! Risk of injury! Never throw batteries into fire! Risk of explosion!

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or solvents/aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany