Technaxx®   *  User Manual

Night Vision Device “Night Vision TX-73”

# The manufacturer Technaxx Deutschland GmbH & Co.KG hereby declares that this device, to which this user manual belongs, complies with the essential requirements of the standards referred to the Directive R&TTE 2014/53/EU. The Declaration of Conformity you find here: www.technaxx.de/ (in bar at the bottom “Konformitätserklärung”). Before using the device the first time, read the user manual carefully.

This device has a rechargeable battery. It must be fully charged before first use. NOTE: Charge the battery of the device every 2–3 month if it is not used!

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks).

Free Email: support@technaxx.de

# Features

( Day-viewing range up to 260m ( Night-viewing range up to 100m ( Integrated IR illumination ( Magnification up to 4 times ( Rechargeable replaceable batteries       ( Record time up to 3.5 hours if batteries are fully loaded ( Saving of video/photo files on MicroSD card up to 32GB ( Video & photo viewing directly on the device possible ( Thread for a tripod

# Technical specifications

| Sensor | 1.3 megapixel CCD |
| --- | --- |
| Resolution | Video 320x240 (50fps) / Photo 2048x1536 |
| Magnification / Viewing range | 4 times / ~260m at day & ~100m at night |
| Viewing angle / Lens Ø / Eye relief | 16° / 40mm / 12mm |
| IR rating / wavelength / effective distance | 0.5mW / 850nm / ~80–100m |
| Close-up focus limit / Diopter adjustment | 1.8m / –4 till +4 |
| Storage | MicroSD / MicroSDHC card up to 32GB |
| Connections | TV out |
| Input power | 1000mAh 5.0V |
| Power supply | Batteries 3x type LIR123A 750mAh 3.7V with protection circuit |
| Charging / record / standby | ~8 hours / ~3.5 hours at day & ~3 hours at night / ~2 weeks |
| Weight / Dimensions | 370g / (L) 18.5 x (W) 8.3 x (B) 5.8cm |
| Package Contents | Night Vision Device TX-73, USB power cable with 2x USB, 3,5mm plug to 1x RCA plug, 3x LIR123A batteries, 8GB MicroSD card with SD card adapter, Storage bag, Cleaning cloth for the lens, Protective cap of the lens, User Manual |

# Night vision device

## View from the left

## View from the right

## Insert the memory card

A MicroSD/MicroSDHC (up to 32GB) must be installed before operating the device. Install it in the device as shown in the following illustration. Ensure, that the contacts of the memory card faces the battery compartment and that the contacts of the memory card are inserted first. Press the memory card into the device until you hear it click in. To remove, push on memory card again. The memory card then slides partially out of the device and can be removed. Note: Format the MicroSD/MicroSDHC memory card (up to 32GB) to FAT32 with computer  before using the device the first time.

## Insert the batteries

On the eyepiece side (back) of the device, open the battery compartment remove the cover by removing the screw completely and then lift off the cover. Install the rechargeable batteries (Type: LIR123A 750mAh 3.7V). Ensure correct polarity of the rechargeable batteries. After inserting the rechargeable batteries, close the battery compartment cover again by replacing the cover and tightening the screw completely. The batteries should then be loaded. To load the rechargeable batteries use the attached USB to power plug with 2x USB. When the device is charging the indicator light is flashing RED.

Note:  If   appears in the display, the batteries no longer have sufficient power. When the batteries are completely empty and the power cable is connected , the RED LED starts flashing after 5–10 Minutes. When the device is not used for 10 minutes it will turn into a power save mode. The indicator light is still on, to show the device is still powered. To get back in working mode press any key.

## Connection to TV

You can connect the device to a TV set with the help of the TV cable (3.5mm plug to 1x RCA plug) supplied with it. Connect the TV cable to the device and the TV set as shown in the following illustration and switch the device on. On the TV set, select the AV port in use as the source. The monitor image will then be displayed directly on the TV set.

# Settings for use

## Hand loop

The hand loop can be adjusted to the size of your hand. Open the hook and loop,  tighten or untighten the hand loop by shorten or length the ends of the straps, then close the hook and loop.

## Functions

The device can be used like conventional binoculars during the day. At night, the IR lens captures the residual light available, boosts it and displays the image produced on the monitor. When looking on the monitor after switching your device via the On/Off button, you will see various symbols beside the motif.

At ① the video mode or photo mode  will be displayed. You can change the recording mode by briefly pressing the 	/ button. In the photo mode, briefly press the button to take a photo. In the video mode you can also start video recording using thebutton. Press theagain to pause the recording. You can end the video recording via the/ button.

② in the video mode shows the maximum recording time and in the photo mode the number of photos still possible. The value in each case depends on the space available on the memory card.

The charge condition of the batteries is shown at ③.

④ shows that a memory card has been installed. If no memory card has been installed, “No card” will be shown at the center of the screen. Note:  The recorded video will be separated in 4:59 minutes each file. The LED indicator light is permanently shining GREEN when in work mode.

## Replay

You can view videos and photos available directly via your device. To do that, press and hold the [◄] button for approx. 3 seconds to switch to the replay mode.

With video recordings the video symbol will be displayed in the lower left corner of the monitor. If there is no symbol visible, a photo is currently being displayed. Use theand / buttons to switch between the shots. Briefly press the ◄ button to start replaying a video. Briefly press the button again to put the replay on hold. To stop replaying the video completely, press the ◄ button for approx. 3  seconds. Switch back to the record mode by pressing and holding the ◄ button for approx. 3 seconds as long as no video replay is running.

Hazard, safety and warning notices

► Incorrect use of the device and accessories can be dangerous for you and others and can damage or destroy your device. We therefore ask you to read and strictly observe the following Hazard, safety and warning notices.

► This device has been designed for private use and is not suitable for commercial purposes.

► The device and accessories may only be used by persons physically and mentally able to operate it safely. Children should be supervised to ensure that they do not play with the device. Hazards for children and persons with limited ability to operate electronic equipment. Always keep accessories and packaging away from children, because the is the danger of electrocution, poisoning and suffocation. 
► Do not place any containers filled with liquid, such as vases or glasses on top or immediately next to the device. Danger of fire and electrocution.

► Do not dismantle, modify or repair your device  Danger of fire and electrocution.

►Switch off the device and remove batteries if a foreign object or liquid has entered the device. Let all parts dry thoroughly. Otherwise danger of fire or electrocution.

► Switch off the device and remove batteries if device has been dropped or housing is damaged. Otherwise danger of fire or electrocution.

► Do not leave your device in places that are susceptible to considerable increases in temperature. The housing and internal parts may be damaged, which in turn could cause a fire.

► Do not cover your device or place it on textiles. This could produce a buildup of heat in the device that can cause deformation of the housing and may represent a fire hazard.

► Do not aim your device at strong sources of light like car headlights, street lights or the direct sunlight.

► When moving your device from a cold into a warm environment, wait at least 3 hours before using it. The device can condense moisture that can damage the electronics when the device is used before it is acclimatised.

► Only place your device on sturdy surfaces. Your device could otherwise fall or topple over, causing damage or injury. Do not place any open ignition sources such as burning candles on or near the device.

► Do not drop or bump device and always handle it with due care. Otherwise it can be damaged.

► Do not operate your device whilst running or driving. You could fall or cause a traffic accident.

► Damage to the electronics or lens caused by extraneous effects such as knocks, falls or others are not covered by the guarantee.

Security and Disposal Hints for Batteries: Hold children off batteries. When a child swallowed a battery go to a doctors place or bring the child into a hospital promptly! Look for the right polarity (+) and (–) of batteries! Always change all batteries. Never use old and new batteries or batteries of different types together. Never short, open, deform or load up batteries! Risk of injury! Never throw batteries into fire! Risk of explosion!

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or solvents/aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany

# Text boxes

Status LEDs

Hand loop

The device has a total of three setting options to sharpen the presentation of the subject. Switch the night vision device on via the On/Off button. Like on binoculars, you can set the device to suit your personal eyesight by turning on the eyepiece.

(1) Once you have adjusted the device to suit your eyesight, you no longer need to change that setting.

(2) The equally rotating lens lets you focus on objects in the viewing angle of your night vision device.

(3) Your night vision device will automatically change to the infrared model at night. This is how you focus via the IR lens.

Note: Avoid aiming your device at strong sources of light like the sun. Your eyes may be injured or the device damaged.

Hand loop

On/Off switch

Tripod thread

Memory card compartment

and TV/DC connection

Objective lens

Battery compartment

Eyepiecece

Video Start/Pause

Taking photos

Tripod thread

IR lens

Objective Lens

Video/Photo

mode button

Record/Replay

Start/Pause/Stop

IR lens